CHAPTER 1 GENERAL INFORMATION

WARNING

The parts of different types/ variants/ versions maybe un-interchangeable, even some parts have almost same appearance. Always refer to Parts Manual of each ATV model for spare parts information and service.

1.1 IMPORTANT INFORMATION

1.2 V.I.N AND ENGINE SERIAL NUMBER

1.3 VEHICLE DIMENSIONS

| 1.1 IMPORTANT INFORMATION PREPARATION FOR REMOVAL PROCEDURES Remove all dirt, mud, dust and foreign material before removal and disassembly. Use proper tools and cleaning equipment. When disassembling the machine, always keep mated parts together. This includes gears, cylinders, pistons and other parts that have been ”mated ”through normal wear. Mated part must always be reused or replaced as an assembly. During machine disassembly, clean all parts and place them in trays in the order of disassembly. This will speed up assembly and allow for the correct installation of all parts. Keep all parts away from any source of fire. REPLACEMENT PARTS Use only genuine parts for all replacements. Use recommended oil and grease for all lubrication jobs. Other brands may be similar in function and appearance, but inferior in quality. GASKETS,OIL SEALS AND O-RINGS Replace all gaskets seals and O-rings when overhauling the engine. All gasket surfaces, oil seal lips and O-rings must be cleaned. Properly oil all mating parts and bearings during reassembly. Apply grease to the oil seal lips. |
| --- |
| LOCK WASHERS/PLATES AND COTTER PINS |
| Replace all lock washers/plates and cotter pins after removal. Bend lock tabs along the bolt or nut flats after the bolt or nut has been tightened to specification. BEARINGS AND OIL SEALS Install bearings and oil seals so that the manufacturer’s marks or numbers are visible. When installing oil seals, apply a light coating of lightweight lithium base grease to the seal lips. Oil bearings liberally when installing, if appropriate. oil seal CAUTION: Do not use compressed air to spin the bearings dry. This will damage the bearing surfaces. Bearing CIRCLIPS Check all circlips carefully before reassembly. Always replace piston pin clips after one use. Replace distorted circlips. When installing a circlip①, make sure that the sharp-edged corner ② is positioned opposite the thrust ③ it receives. See sectional view. ④Shaft CHECKING OF CONNECTIONS Dealing with stains, rust, moisture, etc. on the connector. Disconnect: Connector Dry each terminal with an air blower. Connect and disconnect the connector two or three. Pull the lead to check that it will not come off. If the terminal comes off, bend up the pin ①and reinset the terminal into the connector. Connect: Connector NOTE: The two connectors ” click ” together. Check for continuity with a tester. NOTE: If there is no continuity, clean the terminals. Be sure to perform the steps 1 to 7 listed above when checking the wire harness. Use the tester on the connector as shown. |  |
| WARNING Never run an engine in an enclosed area. Carbon monoxide exhaust gas is poisonous and can cause severe injury or death. Always start engines outdoors. Gasoline is extremely flammable and explosive under certain conditions. Battery electrolyte is poisonous. It contains sulfuric acid. Serious burns can result from contact with skin, eyes or clothing. Always keep alert and wear protection.. Exhaust system components are very hot during and after use of ATV. Never service when the engine is warm or hot. Escaping steam from cooling system or hot oil from the machine can cause severe burns. The engine must be cool before service. Crate of the ATV and parts in the ATV maybe have sharp edge, always pay attention and wear protection. |

CONVERSION TABLE

How to use the CONVERSION TABLE

Use this table to convert METRIC unit data to IMPERIAL unit data.

Ex.

METRIC     MULIPLIER      IMP

**mm    x   0. 3937   =    **in

**cm    x   0.03937   =    **in

CONVERSION TABLE

| METRIC TO IMP |
| --- |
|  | Known | Multiplier | Result |
| Torque | m·kg m·kg cm·kg cm·kg | 7.233 86.794 0.0723 0.8679 | ft·lb In·lb ft·lb In·lb |
| Weight | kg g | 2.205 0.03527 | lb oz |
| Distance | km/h km m m cm mm | 0.6214 0.6214 3.281 1.094 0.3927 0.03927 | mph mi ft yd in in |
| Volume/ Capacity | cc(cm3) cc(cm3) lit(liter) lit(liter) | 0.03527 0.06102 0.8799 0.2199 | oz(IMP liq.) cu·in qt (IMP liq.) gal(IMP liq.) |
| Miscellaneous | kg/mm kg/cm2 Centigrade | 55.997 14.2234 9/5(℃)+32 | lb/in psi(lb/in2 ) Fahrenheit(°F) |

  - V.I.N AND ENGINE SERIAL NUMBER

ATV 260 / 300 / 400-2 /400-2B

Mini / Youth

| 2004 | 2005 |
| --- | --- |
| DEMON | Special Edition - Anniversary |
| Mini / Youth | B-Type |
| ATV400-2 | ATV400-2B |
| 520ATV | 520ATV-B |

  - VEHICLE DIMENSIONS

ATV400-2D

Note.

The on-road equipments (rear view mirror, turn lights, etc.) are not Standard Equipment for USA.

ATV 260 / 300

’05 Model ATV 260 / 300

Demon  ATV 260 / 300 Europe

Mini / Youth

Special Edition - Anniversary

B-Type 260/ 300

B-Type 150/ 200

ATV 400-2

ATV 400-2B

ATV 520

ATV 520-B

ATV 400-2D

NOTES