CHAPTER  2  MAINTENANCE

WARNING

The parts of different types/ variants/ versions maybe un-interchangeable, even some parts have almost same appearance. Always refer to Parts Manual of each ATV model for spare parts information and service.

2.1 PERIODIC MAINTENANCE

2.2 FUEL SYSTEM

2.3 TOE ALIGNMENT

2.4 BRAKING SYSTEM INSPECTION

2.5 SUSPENSION SPRING RPELOAD ADJUSTMENT

2.6 WHEELS

2.7 TIRE PRESSURE

2.8 FRAME, NUTS, BOLTS, FASTENERS

| 2.1 PERIODIC MAINTENANCE |
| --- |
| GENARAL CAUTION Mark on the following chart DL ：Due to the nature of the adjustments marked with a DL on the following chart, it is recommended that service be performed by an authorized dealer. ▲： Service/Inspect more frequently when operating in adverse conditions. Periodic Maintenance Schedule Careful periodic maintenance will help keep your vehicle in the safest, most reliable condition. Inspection, adjustment and lubrication intervals of important components are explained in the following chart on the following pages. Maintenance intervals are based upon average riding conditions and an average vehicle speed of approximately 16km/h (10 miles per hour). Vehicles subjected to severe use, such as operation in wet or dusty areas, should be inspected and serviced more frequently. Inspect, clean, lubricate, adjust or replace parts as necessary. NOTE: Inspection may reveal the need for replacement parts. Always use genuine parts available from your dealer. Service and adjustments are critical. If you are not familiar with safe service and adjustment procedures, have a qualified dealer perform these operations. A = Adjust I = Inspect C = Clean L = Lubricate D = Drain R = Replace T =Tighten to Correct Torque |
|  | Item | Hours | When | Remarks |
|  | Service (Main) Brake System | / | Pre-ride | I |
|  | Auxiliary (Secondary) Brake | / | Pre-ride | I |
|  | Parking Brake | / | Pre-ride | I |
|  | Tires | / | Pre-ride | I |
|  | Wheels | / | Pre-ride | I |
|  | Frame nuts, bolts fasteners | / | Pre-ride | I |
| ▲ | Air Filter-Pre-Cleaner | / | Daily | I C |
|  | Coolant/Level | / | Daily | I |
|  | Coolant | 150 | Annually | R |
|  | Coolant strength | 25 hrs | 3 months | I Inspect strength seasonally |
| ▲ | Air Box Sediment Tube | / | Daily | D |
|  | Headlamp Inspection | / | Daily | C apply dielectric grease to connector when replaced |
|  | Tail lamp inspection | / | Daily | C apply dielectric grease to socket when replaced |
| ▲ | Air Filter-Main Element | 2 | Weekly | I C Replace if necessary |
| ▲ | Transmission Oil Level | 10 | Monthly | I change annually |
|  | Battery Terminals | 10 | Monthly | I C |
|  | Battery fluid level | 10 | Monthly | I |
| DL | Brake pad wear | 2 | Weekly | I |
| ▲ | Gear case Oil | 10 | Monthly | C |
|  |  | 150 | annually | R |
|  | Engine Cylinder Head and Cylinder Base Fasteners | 25 | 3 months | I (re-torque required at first service only) |
| ▲ | General Lubrication all fittings, pivots, cables, etc. | 25 | 3 months | L |
|  | Engine Oil-Level | / | Daily | I |
|  | Engine Oil Change | 30 hrs | 3 months | R Break-in Service at 1 month. Change oil more often in cold weather use. |
| ▲ | Oil Filter | 50 hrs | 6 months | I C |
| ▲ | Engine breather hose | 100 hrs | 6 months | I |
|  | Carburetor Float Bowl | 50 hrs | 6 months | Drain bowl periodically and prior to storage |
|  | Throttle Cable | / | Pre-ride | I |
| DL | Throttle Cable | 50 hrs | 6 months | A L (Grease M) R if necessary |
|  | Shift linkage | 50 hrs | 6 months | I A R if necessary |
| DL | Transmission belt | 50 hrs | 6 months | I R if necessary |
| ▲ | Steering | 50 hrs | 6 months | I L T if necessary |
| ▲ | Rear Axle ( and Bearings) | 50 hrs | 6 months | I L |
| ▲ | Front Suspension | 50 hrs | 6 months | I L T if necessary |
| ▲ | Rear Suspension | 50 hrs | 6 months | I T if necessary |
|  | Spark Plug | 100 hrs | 12 months | I R if necessary |
| DL | Ignition Timing | 100 hrs | 12 months | I Adjust as needed |
| DL | Fuel System | 100 hrs | 12 months | Check for leaks at tank, cap, lines, fuel valve, filter, and carburetor. Replace lines every 2 years. |
| DL | Fuel Filter | 100 hrs | 12 months | R |
|  | Radiator | 100 hrs | 12 months | I R |
|  | Cooling System hoses | 50 hrs | 6 months | I R if necessary |
|  | Spark arrestor | 10 hrs | monthly | C R if necessary |
| DL | Clutches (drive and Driven) | 25 hrs | 3 months | I R R if necessary |
|  | Engine mounts | 25 hrs | 3 months | I T |
| DL | Valve clearance | 100 hrs | 12 months | I A |
| DL | Shift selector box (H/L/R/N) | 200 hrs | 24 months | Change grease every two years |
| DL | Brake fluid Level | / | Pre-ride | I |
|  | Brake fluid | 200 hrs | 24 months | Change every two years |
|  | Idle Speed | / | As Required | A |
| DL | Toe adjustment | / | As Required | Periodic inspection, adjust when parts are replaced |
|  | Headlight Aim | / | As Required | Adjust if necessary |
| ▲ DL | Front drive chain (and sprockets) in transmission (only SDX300 ); | 300 hrs (full time in 4X4), or 1000 hrs ( in 2X4 alternate 4X4 ) | I, Replace if necessary |
| ▲ DL | Ball joint (A arm- strut) | 10 hrs | monthly | I, (for damage, wear, and play) R. Replace if necessary |

LUBRICANT AND FLUID

|  | Item | Lube Rec | Method | Frequency |
| --- | --- | --- | --- | --- |
|  | Engine Oil | SAE 15W/40 SE | Add to proper level on dipstick | Check level daily |
|  | 2. Brake Fluid | DOT 3 Only | Maintain level Between fill lines. See “7.CONTROL” | As require; change every two years or 200 hours |
|  | 3. Transmission Oil | SEA 80W/90GL5 | Add to proper level on dipstick | Change annually or at 100 hours |
|  | 4.Rear Gear case oil | SEA 80W/90GL5 | Add to proper level | Change annually or at 100 hours |
|  | 5. Front Gear case oil ( SDX30-0 ) | SEA 80W/90GL5 | Add to proper level | Change annually or at 100 hours |
| ▲ | 6. Front A-arm pivot Shaft | Grease | Locate fitting on pivot shaft and grease with grease gun | Every 3 months or 50 hours ( Except Maintenance-Free A-arm pivot ) |
| ▲ | 7.Steering Post Bushings | Grease | Locate fitting on pivot shaft and grease with grease gun | Every 3 months or 50 hours |
| ▲ | 8.Front Wheel bearings | Grease (high temperature resist) | Inspect and replace bearings if necessary | Semi-annually |
|  | 9.Tie rods | Grease | Locate fittings and grease | Semi-annually |
|  | 10.Shift Linkages | Grease | Locate fittings and grease | Semi-annually |
| ▲ | 11.Ball joints | Inspect | Inspect and replace it if necessary | Semi-annually |
| ▲ | 12.Rear Axle Bearing | Grease | Locate fittings and grease | Every 3 months or 50 hours |
| ▲ | 13.Swing Arm Bearing | Grease | Locate fittings and grease | Monthly or 20 hours |
| ▲ | 14.Throttle Cable | Grease M | Grease, inspect and replace it if necessary | Monthly or 20 hours |
|  | 15. Rear prop shaft U-joint | Grease | Locate fittings and grease | Every 3 months or 50 hours |
|  | 16. Rear prop shaft yoke | Grease | Locate fittings and grease | Every 3 months or 50 hours |
|  | 17. Front prop shaft U-joint ( SDX300) | Grease | Locate fittings and grease | Every 3 months or 50 hours |
|  | 18. Front prop shaft yoke ( SDX300) | Grease | Locate fittings and grease | Every 3 months or 50 hours |
|  | 19. Inner and outer CV-Joints (SDX300) | Grease M | Grease, inspect and replace it if necessary | Every 3 months or 50 hours |
| ▲ | 这一行去掉，下图中的链条也去掉 | Lubricate | I C L Adjust or/ and replace if necessary | Weekly |
|  | 21. A-arm pivot shaft | Grease | Locate fittings and grease | Every 3 months or 50 hours |

Lubrication Recommendations

NOTE:

- More often under severe use, such as wet or dusty conditions.

- Grease: Light weight lithium-soap grease.

- Grease M：Molybdenum disulfide (MoS2 ) grease (water resistant).

- When suspension action becomes stiff or after washing.

- Hours are based on 10 mph(16Km/h) average.

2.2 FUEL SYSTEM

WARNING

Gasoline is extremely flammable and explosive under certain conditions.

Always stop the engine and refuel outdoors or in a well ventilated area.

Do not smoke or allow open flames or sparks in or near the area where refueling is

performed or where gasoline is stored.

Do not overfill the tank. Do not fill the tank neck.

If you get gasoline in your eyes or if you swallow gasoline, see your doctor immediately.

If you spill gasoline on your skin or clothing, immediately wash it off with soap and water and change clothing.

Never start the engine or let it run in an enclosed area. Gasoline powered engine exhaust fumes are poisonous and can cause loss of consciousness and death in a short time.

Never drain the float bowl when the engine is hot. Severe burns may result.

ATV 260/ 300/400-2

YOUTH/MINI ATV

B-TYPE ATV/ATV400-2B

FUEL LINES

Check fuel lines for signs of wear, deterioration, damage or leakage. Replace if necessary.

Be sure fuel lines are routed properly and secured with cable ties.

CAUTION: Make sure lines are not kinked or pinched.

Replace all fuel lines every two years.

FUEL FILTER

The fuel filter should be replaced in accordance with the Periodic Maintenance Chart or whenever sediment is visible in the filter.

- Shut off fuel supply at fuel valve.

- Remove line clamps at both ends of the filter.

- Remove fuel lines from filter.

- Install new filter and clamps onto fuel lines with arrow pointed in direction of fuel flow.

- Install clamps on fuel line.

- Turn fuel valve ON.

- Start engine and inspect for leaks.

- Reinstall fuel tank.

ATV 260/ 300

ATV 260/ 300

FUEL VALVE AND STRAINER SCREEN FOR B-TYPE ATV/ATV400-2B

Fuel strainer screen cleaning:

- Remove the fuel tank.

- Drain the gasoline into an approved fuel container. Remove the two mounting bolts, collars and the fuel valve.

- Remove the O-ring and fuel strainer screen.

- Clean the strainer screen with non-flammable or high flash point solvent. Dry the strainer screen thoroughly.

- Install the strainer screen and a new O-ring onto the valve.

- Install the fuel valve onto the fuel tank.

- Install the collars and mounting bolts, and tighten the bolts securely.

NOTE

After installing the fuel valve and connecting the fuel line, refill the fuel tank and turn the fuel valve ON and check that there is no fuel leaking.

WARNING

Always pay attention to the fittings of the plastic gas tank during fuel lines service. Don’t pull the line from the tank directly for removal. Inspect fittings and tank body for looseness, nicks, and scratches. Replace gas tank if necessary.

VENT LINES AND ROLL OVER VALVE*

- Check fuel tank, oil tank, carburetor, battery, and transmission vent lines for signs of wear, deterioration, damage or leakage. Replace every two years.

- Be sure vent lines and drain lines are routed properly toward the ground and secured with cable ties. CAUTION: Make sure lines are not kinked or pinched

*NOTE. On some models, there is a Roll-Over Valve on the end of the gas tank vent line. Make sure the ↑ mark on the R-O Valve is upwards.

B-TYPE ATV

  - TOE ALIGNMENT

METHOD: STRAIGHTEDGE OR STRING

Be sure to keep handlebars centered

NOTE:  String should just touch side surface of rear tire on each side of the ATV.

Measure from string to rim at front and rear of rim.

Rear rim measurement (A) should be 1/16" to 1/8" (1.5 to 3 mm) more than front rim measurement (B).

NOTE: The steering post arm (frog) can be used as an indicator of whether the handlebars are straight. The frog should always point straight back from the steering post when handlebars are straight.

WARNING: Always pay attention to tie rods assembly, Both ends must screw in same and enough threads length.

2.4 BRAKING SYSTEM INSPECTION

The following checks are recommended to keep the braking system in good operating condition. Service life of braking system components depends on operating conditions. Inspect brakes in accordance with the maintenance schedule and before each ride.

(Keep fluid level in the master cylinder reservoir to the indicated level on reservoir.

(Use DOT 3 brake fluid.

NOTE:  Use new brake fluid or brake fluid from a sealed container to avoid contamination to system.

(Check brake system for fluid leaks.

(Check brake for excessive travel or spongy feel.

(Check friction pads for wear, damage and looseness.

(Check surface condition of the disc.

BRAKE  PAD  INSPECTION

(Pads should be changed when friction material is worn to 3/64" (1mm).

HOSE/FITTING  INSPECTION

Check braking system hoses and fittings for cracks, deterioration, abrasion, and leaks. Tighten any loose fittings and replace any worn or damaged parts.

FOOT BRAKE ADJUSTMENT

NOTE

On USA ATV 260 / 300 and B-type, foot brake is an AUXILIARY brake.

On European ATV 260 / 300 and B-type , foot brake is the service brake (main brake)

Use the following procedure to inspect the hydraulic foot brake system and adjust or bleed if necessary.

Foot control brake is only for ATV 260 / 300

Adjusting brake pedal for B-Type

If the push rod joint is reinstalled, adjust the push rod length so that the distance between the centers of the master cylinder lower mounting bolt hole and joint pin hole is 83±1mm.After adjustment, tighten the joint nut.

1. First check foot brake effectiveness by applying a 25 kg (50 lb). (Approx) downward force on the pedal.

The top of the pedal should be at least 1  inch, (25 .4m m) above the surface of the footrest.

If less than one inch, two things must be examined:

Free Play:

Free play of the brake pedal should be 1/8-1/4 inch (3-6mm).

If free play is excessive, inspect pedal, linkage, and master cylinder for wear or damage and replace any worn parts.

Bleeding:

If free play is correct and brake pedal travel is still excessive, air may be trapped some where in the system. Bleed the hydraulic brake system in a conventional manner, following the procedure outlined in the Brake chapter.

FOOT BRAKE TESTING

The foot brake should be checked for proper adjustment.

Support the rear wheels off the ground. While turning the rear wheels by hand, apply the auxiliary footbrake. This brake should not stop the wheels from turning until the lever is half way between its rest position and bottoming on the footrest.

MECHANICS PARKING BRAKE FOR EUROPE ATV 260 / 300 / 400-2

Checking

Although the parking brake has been adjusted at the factory, the brake should be checked for proper operation. The mechanical brake must be maintained to be full functional.

CONTROLS

Check controls for proper operation, positioning and adjustment.

Brake control and switch must be positioned to allow brake level to travel throughout entire range without contacting switch body.

Note: burnishing procedure is also applicable for parking brake. See CHAPTER 7 BRAKES.

↑adjust on the lever    ATV 260/300

1. With the engine off, apply the parking brake lever and attempt to move the ATV.

2. If the rear wheels are locked, it is adjusted properly.

3. If the wheels are not locked, it must be adjusted.

To adjust (set up) the mechanical parking brake, use the following procedure

Note: The adjusting on the caliper is for the wear out of the pads.

1. With the engine off, loosen the adjustor on the lever.

2. Loosen the jam nut of the adjuster on the caliper.

3. Turn the adjuster (bolt) CW (clockwise) by hand till the pad touch the brake disc, turn the adjuster bolt CCW (counterclockwise) by 1/4 to one turn for 10 to 20mm free play at the end of the parking lever.

4. Tighten the jam nuts securely against the adjusters.

5. Make sure the rear wheels turns freely without dragging.

6. Turn the adjustor (the one on the lever) and apply the lever. While adjusting, it is important you apply the lever back and forth for operation, free play and the locking of the parking position.

7. Make sure the rear wheels turns freely without dragging and parking brake works properly.

CAUTION Don’t over tighten the adjustor. Free play of the lever: 20mm.

8. Field test for parking. It must be capable of holding the laden ATV stationary on an 18% up and down gradient.

A temporary adjusting can also be done to the brake cable on the parking lever side by turn the adjuster (nut) directly. But the adjust range is limited. Always do the procedure 1 to 8 when necessary.

↑ adjust on the lever   B-type ATV

ATV400-2B

Adjusting can also be done to the brake cable on the parking lever side by turn the adjuster (nut) directly.

↑ adjust on the caliper   ATV 260/300

ATV400-2

ATV400-2B

↑ adjust on the caliper   B-type ATV

DRUM BRAKE FOR ATV 50-150

The front brakes are located on the right handlebar. and are operated by the right hand. The front brakes are mechanical drum type brakes which are activated by one lever only.

Brake shoes

- The standard thickness of lining is 5/32”(4mm)

- Shoes should be changed when friction material (lining) is worn to 2.5 mm.(a)

- Replace the brake shoes as a set if either is worn to the limit.

Brake drum

- The standard brake drum inside diameter is 110mm, the limit is 110.5mm.

- Measure the brake drum inside diameter(a)

Drum Brake

Checking

Although the front brake has been adjusted at the factory, the brake should be checked for proper operation. The mechanical brake must be maintained to be fully functional.

1. With the engine off, apply the right hand brake lever and attempt to move the ATV.

2. If the both front wheels are locked, it is adjusted properly.

3. If the wheels or one wheel are/is not locked, it must be adjusted.

Adjusting

To adjust (set up) the mechanical drum brake, use the following procedure.

1. Loosen the jam nuts of the

adjuster on the right hand of

right and left brake cable.

2. Turn the both adjusters keep the rock arm on the lever balance until 1/8” (2to3mm) free play is achieved at the brake lever.

NOTE: Replace the brake shoes as a set either is worn to the limit.

NOTE: While adjusting free play, it is important you apply the lever back and forth.

3. Tighten the jam nuts securely against the adjusters.

If the right hand adjustment is inadequate to attain the proper brake free-play gap, make adjustment at the middle of the cables adjuster jam nuts.

NOTE: Apply the front brake a number of times to ensure the wheels lock and the brake light illuminate properly.

4. Make sure the right and left brake are balance after the adjustment of the front brakes by test at low speed. Contact your

dealer for proper diagnosis and repairs.

5. If adjusting the cables does not attain proper brake performance and free-play, the brake shoes must be replaced.

Note: After the adjusting, the adjustment distance of the cables and the angle of the drum levers between the right and left brake must be same.

2.5 SUSPENSION SPRING RPELOAD ADJUSTMENT

Operator weight and vehicle loading affect suspension spring preload requirements. Adjust as necessary.

FRONT SUSPENSION

Compress and release front suspension. Damping should be smooth throughout the range of travel.

Check all front suspension components for wear or damage.

Inspect from strut cartridges for leakage. Shock spring preload can not be adjusted, replace if necessary.

REAR SUSPENSION

Compress and release rear suspension. Damping should be smooth throughout the range of travel. Check all rear suspension components for wear or damage.

Inspect	shock for leakage

Shock spring preload can be adjusted using the shock spanner wrench.

★This design is not available for all type.

2.6 WHEELS

Inspect all wheels for runout of damage.

Check wheel nuts and ensure they are tight.

Do not over tighten the wheel nuts.

WHEEL, HUB TORQUE TABLE

| Item | Specification |
| --- | --- |
|  | Youth/Mini ATV | ATV260 300 and B-Type |
| Front Wheel Nuts | 35-40 N.m | 26-30 Ft.Lbs | 20 Ft.Lbs | 27 N.m |
| Rear Wheel Nuts | 35-40 N.m | 26-30 Ft.Lbs | 50 Ft.Lbs | 69 N.m |
| Front Spindle Nut | 45-50 N.m | 33-37 Ft.Lbs | Refer to FRONT HUB INSTALLATION |
| Rear Hub Retaining Nut | 50/80 cc | 80-85 N.m | 60-62 Ft.Lbs | 80 Ft.Lbs | 110.6 N.m |
|  | 100/125/150 cc | 110 N.m | 81 Ft.Lbs |  |  |

WHEEL REMOVAL

- Stop the engine, place the transmission in gear

And lock the parking brake.

2.  Loosen the wheel nuts slightly.

- Elevate the side of the vehicle by placing a suitable stand under the footrest frame.

4.  Remove the wheel nuts and remove the wheel.

WHEEL INSTALLATION

- With the transmission in gear and the parking Brake locked, place the wheel in the correct Position on the wheel hub. Be sure the valve stem is toward the outside and rotation arrows on the tire point toward rotation.

- Attach the wheel nuts (for ATV 260 / 300 and B-Type) / bolts ( for ATV 50-150) and finger tighten them.

Install as shown at right for front or rear wheels.

- Lower the vehicle to the ground.

4. Securely tighten the wheel nuts to the proper Torque listed in the table above. On rear wheel nuts, Make sure tapered end of nut goes into taper on wheel.

ATV 260/300 and B-Type

CAUTION:

If wheels are improperly installed it could affect Vehicle handling and tire wear.

2.7 TIRE PRESSURE

TIRE INSPECTION

CAUTION :

( Maintain proper tire pressure. Refer to the warning tire pressure decal applied to the vehicle.

(Improper tire inflation may affect ATV maneuverability.

(When replacing a tire always use original equipment size and type and replace in pairs, especially in SDX300 model.

( The use of non- standard size or type tires may affect ATV handling and cause machine damage, especially in SDX300 model.

TIRE TREAD DEPTH

Always replace tires when tread depth is worn to 1/8" (3mm ) or less.

Tire Pressure Inspection

|  | Front | Rear |
| --- | --- | --- |
| 260/300 | 4PSI (27±0.5KPa) | 4PSI (27 ±0.5KPa) |
| B-Type 150 / 200 | 5PSI （35KPa） | 5PSI （35KPa） |
| Youth/ Mini |  |  |
| 400ATV-2 400ATV-2B |  |  |

WARNING Operating an ATV with worn tires will increase the possibility of the vehicle skidding easily with possible loss of control.

Worn tires can cause an accident.

Always replace tires when the tread depth measures 1/8" (3mm ) or less.

2.8 FRAME , NUTS, BOLTS, FASTENERS

Periodically inspect the tightness of all fasteners in accordance with the maintenance schedule. Check that all cotter pins are in place. Refer to specific fastener torques listed in each chapter.

| ATV 260 / 300 and B-Type |  |  |  |
| --- | --- | --- | --- |
| Item | Torque （Ft-Lb） | Torque (Nm) | Remarks |
| EARLY DESIGN* Handlebar Clamp Nut M6 | 12 | 16 | Only ATV 260 early model |
| Handlebar Clamp Nut M8 | 18 | 25 |  |
| Nut M10X1.25 Attaching Tie Rod to Steering column | 26-30 | 35-41 |  |
| Nut M10X1.25 Attaching Tie Rod to Front Absorber Strut body | 26-30 | 35-41 |  |
| Tie Rod Jam Nut M12 | 13 | 17 |  |

| EARLY DESIGN* Bolt M10 Attaching A-Arm and Frame | 30 | 41 | LT* Only ATV 260 early model |
| --- | --- | --- | --- |
| MANTENANCE-FREE PIVOT DESIGN Bolt M12 Attaching A-Arm and Frame | 37-44 | 50-60 | LT* |
| Nut M10X1.25 Attaching A-Arm to Ball Joint Stud | 22-25 | 30-35 |  |
| Screw M6 Attaching Ball Joint Mounting Bracket to Front Absorber Strut body (MacPherson) | 8 | 11 | LT* |
| Swing Arm Pivot Left | 14 | 19 | Refer to Swing Arm Assembly Installation ，4.2 SWING ARM，CHAPTER 4A CHASSIS |
| Swing Arm Pivot Right | 120 | 165 |  |
| Threaded Pivot Nut (for swing arm) | 120 | 165 |  |
| Nut M14X1.5 Attaching Front Absorber to Frame (MacPherson) | 15-18 | 21-25 | LT* |
| Nut M8 Binding Front Absorber and Front Absorber Strut body (MacPherson) | 15 | 21 | LT* |
| Bolt M8 Attaching Front Caliper to Front Absorber Strut body | 18 | 25 | LT* |
| Bolt M8 Attaching Upper Steering Clamp to Frame | 12 | 16 |  |
| Nut M8 Attaching Lower Steering Bearing Retainer to Frame | 12 | 16 |  |
| Nut M10X1.25 Attaching Front Wheel to Front Wheel Hub | 20 | 27 |  |
| Front （Drive） Axle Nut | Refer to FRONT HUB INSTALLATION |
| Screw M8 Attaching Front Brake Disc to Front Wheel Hub | 18 | 25 | LT* |
| Nut M10X1.25 Attaching Rear Brake Disc to Rear Brake | 22-25 | 30-35 | LT* |
| Rear Axle Nut M20X2 (for swing arm) | 80 | 110.6 |  |
| Rear Hub Retaining Nut M20X1 （for IRS） | 101 | 137 |  |
| Nut M10X1.25 Attaching Rear Caliper to Axle Tube | 18 | 25 | LT* |
| Bolt M12x30 Attaching Axle Tube and Swing arm to Rear Gear-box | 60 | 80 |  |
| Bolt M12x35 Attaching Axle Tube to Swing arm | 60-66 | 80-90 |  |

LT*---Apply Loctite™ 242

NOTES