CHAPTER  3 A  ENGINE

260cc / 300 cc /400 cc

3.1 MAINTENANCE SPECIFICATIONS

3.1.1 SPECIFICATIONS

3.1.2 TIGHTENING TORQUES

3.2 PARTS INSPECTION AND SERVICE

3.2.1 VALVE CLEARANCE ADJUSTMENT

3.2.2 IDLING SPEED ADJUSTMENT

3.2.3 SPARK PLUG INSPECTION

3.2.4 COMPRESSION PRESSURE

3.2.5 ENGINE OIL LEVEL INSPECTION

3.2.6 COOLANT LEVEL INSPECTION

3.3 CYLINDER HEAD

3.4 CAMSHAFT AND ROCKER ARMS

3.5 VALVES AND VALVE SPRINGS

3.6 CYLINDER AND PISTON

3.7 V-BELT, CLUTCH AND SECONDARY/PRIMARY SHEAVE

3.8 A.C. MAGNETO AND STARTER CLUTCH

3.9 OIL PUMP

3.10 CRANKCASE AND CRANKSHAFT

3.11 COOLING SYSTEM

3.11.1 RADIATOR

3.11.2 WATER PUMP

3.11.3 THERMOSTAT

3.12CARBURETOR

3.1 MAINTENANCE SPECIFICATIONS

3.1.1SPECIFICATIONS

| Item | Standard | Limit |
| --- | --- | --- |
| Cylinder head : Warp limit. |  | 0.03 mm |
| Cylinder: Bore size | 260:70.000- 70.014 mm | 260:70.025 mm |
|  | 300:72.500- 72.514 mm | 300;72.525 mm |
|  | 400: 80.000- 80.014 mm | 400:80.025mm |
| Out of round limit |  | 0.03 mm |
| Camshaft: Cam dimensions Intake "A" "B" "C" Exhaust "A" "B" "C" Camshaft runout limit |  | 36 .545- 36 .645 mm 30.021-30.121 mm 6.524 mm 36 .547- 36 .647 mm 30 .067- 30.167 mm 6.48 mm ….. | 36 .45 mm 29.92 mm … 36 .45 mm 29 .97 mm … 0.03m m |
| Cam chain: Cam chain type/No. of links | 260/300: DID SC.A-0404A SDH/104 400:DID SC.A-0404A SDH/108 | … |
| Rocker arm /rocker armshaft: Rocker arm inside diameter Rocker shaft outside diameter Rocker arm - to- rocker arm shaft clearance | 12 .000- 12 .018 mm 11.981- 11.991 mm 0.009- 0.012 mm | 12 .03 mm 11.95 mm … |
| Valve, Valve seat, Valve guide: Valve clearance (cold) IN EX Valve dimensions | 0.08-0.12 mm 0.16-0.20 mm | … … |
| "A" head diameter IN EX "B" face width IN EX "C " seat width IN EX "D" margin thickness IN EX Stem outside diameter IN EX Guide inside diameter IN EX | 33.9-34.1mm 28.4-28.6mm 3.394-3 .960mm 3.394-3.960 mm 0.9-1.1mm 0.9-1.1 mm 0.8-1.2 mm 0.8-1.2 mm 5.975- 5.990 mm 5.960-5.975 mm 6.000- 6.012 mm 6.000- 6.012 mm | … … … … … … … 5.94 mm 5.92 mm 6.05 mm 6.05 mm |

| Item | Standard | Limit |
| --- | --- | --- |
| Stem-to-guide clearance IN EX Stem runout limit IN Valve seat width EX | 0.010- 0.037 mm 0.025-0.052 mm … 0.9-1.1 mm 0 .9-1.1 mm | 0.08 mm 0.1 mm 0.01 mm 1.6 mm 1.6 mm |
| Valve spring : Free length (Inner) IN/EX (Outer) INEX Set length (valve closed) (Inner) IN/EX (Outer) IN/EX Com pressed pressure (Inner) IN/EX (Outer) IN/EX Tilt limit (Inner) IN/EX (Outer) IN/EX | 38.1 mm 36.93 mm 30.1 mm 31.6 mm 7 .8- 9.0 kg 37.22-42 .83 kg … … | 361 mm 35.0 mm … … … … 2.5°/1.7mm 2.5°/1.7mm |
| Piston: Piston to cylinder clearance Piston size "D" Measuring point "H" Piston pin bore inside diameter |  | 260 /300: 0.02 - 0.04 mm 260;69.965-69.980 mm 300;72.465-72.480 mm 5mm 17.004-17.015 mm 16 .991-17 .000 mm | 0.15m m … … 17.045 mm 16 .975 mm |
| Piston pin outside diameter |  |  |
| Piston: Piston to cylinder clearance Piston size "D" Measuring point "H" Piston pin bore inside diameter |  | 400: 0.02 - 0.049mm 79.965-79.980 mm 5mm 18.004-18.015 mm 17 .991-18 .000 mm | 0.15m m … … 18.045 mm 17 .975 mm |
| Piston pin outside diameter |  |  |
| Piston rings : Top ring : Type End gap (installed) Side clearance (installed ) 2nd ring : Type End gap (installed) Side clearance Oil ring : End gap (installed) | 260 /300: Barrel 0.15- 0 .30 mm 0.04- 0.08 mm Taper 0 .30- 0 .45 mm 0.03 - 0.07 mm 0 .2- 0.7 mm | … 0 .45 mm 0 .12 mm … 0.7 mm 0.12 mm … |
| Piston rings : Top ring : Type End gap (installed) Side clearance (installed ) 2nd ring : Type End gap (installed) Side clearance Oil ring : End gap (installed) | 400: Barrel 0.2-0.35 mm 0.03-0.065 mm Taper 0.28-0.48 mm 0.02-0.052 mm 0. 15-0.4 mm | … 0.5 mm 0.1 mm … 0.73 mm 0.1 mm … |
| Crankshaft: | 59.95-60.00 mm 0.03 mm 0.35- 0.85 mm | … … … |
| Crank width "A" Runout limit "C " |  |  |  |
| Big end side clearance "D" |  |  |

| Item | Standard | Limit |
| --- | --- | --- |
| Automatic centrifugal clutch: Clutch shoe thickness Clutch hosing inside diameter Clutch shoe spring free length W eight outside diameter Clutch- in revolution | 3.0 mm 135 mm 2 8.1 mm 20 mm 2 ,100- 2,700 r/m in | 2.0 mm 135 .5 mm … 19 .5 mm … |
| V-belt: V-belt width | 22.6 mm | 21.0 mm |
| Carburetor: Type I.D. mark Ventuly outside diameter Main jet (M .J) Jet needle (M .A.J) Throttle valve size (J.N) Pilot air jet (Th .V) Needle jet (P.A.J.1) Pilot outlet (N.J) Pilot jet (P.O) Bypass (B.P) Pilot screw (P.S) Valve seat size (V.S) Starter jet 1 (G.S.1) Starter jet 2 (G.S.2) Float height (F.H) Engine idle speed Intake vacuum | CVK 1000-L06-0000 T VH- 052D φ30 # 128 N7AJ 10° φ1.2 φ2.1 φ0.95 # 38 φ0.7x4 1*3/8 φ1.2 # 42 φ0 .9 ＞3.0 1,350-1,650 r/m in 220-260 mmHg | … … … … … … … … … … … … … … … |
| Oil pump: Type Tip clearance Side clearance Housing and rotor clearance | Trochoid type 0.1- 0 .34 mm 0.013- 0.03 6 mm 0 .04- 0.09 mm | 0 .4 mm 0 .15 mm 0 .15 mm |

| Item | Standard | Limit |
| --- | --- | --- |
| Radiator: Type Width/height/thickness Radiator cap opening pressure Radiator capacity Reservoir tank capacity | Cooling fin with electric fan 260 /300: 288/238/42 mm 400: 360/246/68 m 110-140kPa (1.1-1.4kg/cm 2, 1.1-1.4bar) 2 L 0 .35 L | … … … … … |
| Thermostatic valve: Valve opening temperature Valve full open temperature Valve full open lift | 70 .5- 73 .5℃ 85 ℃ 3 mm |  |

3.1.2TIGHTENING TORQUES

| Part to be tightened | Part name | Thread size | Q’ty | Tightening Torque N.m m.kg | Remarks |
| --- | --- | --- | --- | --- | --- |
| Oil check bolt Exhaust pipe stud bolt Spark plug Cam sprocket cover Cylinder head and cylinder Cylinder head and cylinder (Cam chain side) Valve cover Rotor Valve adjuster locknut Cam shaft bearing stopper Cam sprocket Cam chain tensioner (Body) (Plug) Guide stopper 2 Water pump housing cover Hose joint Thermostatic valve cover Filer neck supporting Oil pump Oil pump cover Drain plug Carburetor joint Carburetor joint and carburetor Fuel pump Exhaust pipe assembly Crankcase (left and right) Drain bolt Oil filer Crankcase cover (left) Magnet cover | _ _ _ Bolt Nut Bolt Bolt Nut Nut Bolt Bolt Bolt Bolt Bolt Bolt _ Bolt Bolt Screw Bolt Bolt Bolt Bolt _ Nut Bolt Bolt Bolt Bolt _ | M 6 M 8 M12 M 6 M 8 M 6 M 6 M16 M 6 M 6 M10 M 6 M8 M 6 M 6 M 6 M 6 M 5 M 6 M 3 M 35 M 6 M 6 M6 M8 M 6 M 8 M 14 M 6 M 6 | 1 2 1 2 4 2 5 1 2 2 1 2 1 1 3 2 2 1 2 1 1 2 2 2 2 9 1 1 10 10 | 10 13 18 10 22 10 10 80 14 8 60 10 8 10 10 7 10 5 7 1 32 10 10 10 20 10 22 3 10 10 | 1.0 1.3 1.8 1.0 2 .2 1.0 1.0 8.0 1.4 0 .8 6.0 1.0 0.8 1.0 1.0 0.7 1.0 0 .5 0.7 0.1 3 .2 1.0 1.0 1.0 2.0 1.0 2 .2 0 .3 1.0 1.0 |  |

| Part to be tightened | Part name | Thread | Q’ty | Tightening torque | Remarks |
| --- | --- | --- | --- | --- | --- |
|  |  | size |  |  |  |
|  |  |  |  | Nm | m.kg |  |
| Cover (oil pump) | Bolt | M 6 | 2 | 12 | 1.2 |  |
| Timing check plug | P lug | M 16 | 1 | 8 | 0 .8 |  |
| One way clutch | _ | M 8 | 3 | 30 | 3.0 |  |
| Clutch housing | Bolt | M 14 | 1 | 60 | 6.0 |  |
| Grease stopper (Primary sheave) | _ | M 4 | 4 | 3 | 0 .3 |  |
| Primary fixed sheave | _ | M 14 | 1 | 60 | 6.0 |  |
| Clutch carrier assembly | _ | M 36 | 1 | 90 | 9.0 |  |
| Stator | _ | M 5 | 3 | 7 | 0.7 |  |
| Pick up coil | _ | M 5 | 2 | 7 | 0.7 |  |
| Starter motor | Bolt | M 6 | 2 | 10 | 1.0 |  |
| Thermo switch | _ | M 16 | 1 | 23 | 2 .3 |  |
| Thermo unit | _ | P t1/8 | 1 | 8 | 0 .8 |  |

3.2 PARTS INSPECTION AND SERVICE

| 3.2.1VALVE CLEARANCE ADJUSTMENT |  |
| --- | --- |
| NOTE: Valve clearance adjustment should be made with the engine cool, at room temperature. When the valve clearance is to be measured or adjusted, the piston must be at Top Dead Center (T.D.C.) on the compression. |  |
| 1. Remove : (Crankcase cover |  |
| 2. Remove : (Spark plug ( Valve cover (intake side) (Valve cover (exhaust side) |  |
| 3. Remove: (Timing check plug |  |
| 4.Measure: (Valve clearance Out of specification → Adjust. Valve clearance (cold): 260 / 300: Intake valve 0.08- 0.12m m Exhaust valve 0.16- 0 .20mm 400: Intake valve 0.08- 0.12m m Exhaust valve 0.13- 0.16mm |  |
| Measurement steps: (Rotate the primary fixed sheave counterclockwise to align the slit “a” on the rotor with the stationary pointer “b” on the crankcover 1 when the piston is Top Dead Center (TDC). (Measure the valve clearance by using a feeler gauge. |  |
| 6. Adjust (Valve clearance |  |
| Adjustment steps: (Loosen the locknut ( (Turn the adjuster ③ in or out with the valve adjusting tool ( until specified clearance is obtained . |  |
| Turning in → Valve clearance is decreased Turning out → Valve clearance is increased |  |
| (Hold the adjuster to prevent it from moving and tighten the locknut. |  |
| (Measure the valve clearance. (If the clearance is incorrect, repeat above steps until specified clearance is obtained. |  |
| 7. Install: (Valve cover (intake side) ( (O-ring( |  |
| 8 . Install: (Valve cover(exhaust side) (O-ring (Spark plug (Timing check window screw (Crankcase cover 8N.m( 0.8m.kg) |  |
| 3.2.2 IDLING SPEED ADJUSTMENT |  |
| 1. Start the engine and let it warm up for several minutes. |  |
| 2 . Attach : ( Inductive tachometer to the spark plug lead. |  |
| 3. Check: (Engine idling speed |  |
|  | Out of specification → Adjust. Engine idling speed: 1,350-1,650 r/min |  |
| 4. Adjust: ( Engine idle speed |  |

| Adjustment steps: (Turn the pilot screw ( until it is lightly seated. (Turn the pilot screw out by the specified number of turns. |  |
| --- | --- |
|  | Pilot screw: 1 3/8 turn out |  |
| ( Turn the throttle stop screw ( in or out until the specified idling speed is obtained. |  |
| Turning in → Idling speed is increased. Turning out → Idling speed is decreased. |  |
| 3.2.3SPARK PLUG INSPECTION |  |
| 1.Remove : ( Spark plug cap ( Spark plug |  |
| CAUTION: Before removing the spark plug, use compressed air to blow away any dirt accumulated in the spark plug wells to prevent it from falling into the cylinder. |  |
| 1. Check: (Spark plug type Incorrect Replace. |  |
|  | Standard spark plug: DR8EA (NGK) |  |
| 2.Inspect: (Electrode ( Wear/ damage Replace. (Insulator ( Abnormal color Replace. Normal color is a medium - to- light tan color. |  |
| 3.Clean: (Spark plug (with spark plug cleaner or wire brush) |  |
| 4.Measure: (Spark plug gap ③ (with a wire gauge) Out of specification Adjust gap. |  |
|  | Spark plug gap : 0.6-0.7 mm |  |

| 6. Install: (Spark plug |  |
| --- | --- |
| NOTE: Before installing a spark plug, clean the Gasket surface and plug surface. |  |
| 3.2.4COMPRESSION PRESSURE |  |
| MEASUREMENT |  |
| NOTE : Insufficient compression pressure will result in performance loss. |  |
| 1. Check: (Valve clearance Out of specification Adjust. Refer to “CALCE CLEARANCE ADJUSTMENT” section. |  |
| 2. Start the engine and let it warm up for several minutes. |  |
| 3. Turn off the engine. |  |
| 4. Remove: (Spark plug |  |
| Before removing the spark plug, use com pressed air to blow away any dirt accumulated in the spark plug well to prevent it from falling into the cylinder. |  |
| 5. Attach: (Compression gauge( |  |
| 6. Measure: (Compression pressure |  |
| If it exceeds the maximum pressure allowed→ Inspect the cylinder head, valve surfaces and piston crown for carbon deposits. |  |

| If it is below the minimum pressure → Squirt a few drops of oil into the affected cylinder and measure again. Follow the table below. |  |
| --- | --- |
| Compression pressure (With oil applied into cylinder) |  |
| Reading | Diagnosis |  |
| Higher than without oil | Worn or damaged pistons |  |
| Same as without oil | Possible defective ring (s), valves, cylinder head gasket or Piston →Repair. |  |
|  | Compression pressure(at sea level): Standard: 1,400 kPa (14Kg/cm2, 14 bar) Minimum : 1,120 kP a (11.2 kg /cm 2, 11.2 bar) |  |
| Measurement steps : (Crank the engine with the throttle wide open until reading on the compression gauge stabilizes. |  |
| WARNING : Before cranking the engine, ground all spark plug leads to prevent sparking. |  |
| 8. Install: ( Spark plug |  |
| 3.2.5ENGINE OIL LEVEL INSPECTION |  |
| 1. Start the engine and let it warm up for a few minutes . |  |
| 2. Turn off the engine. |  |
| 3. Inspect: (Do not thread dipstick in) (Engine oil level Oil level should be between maximum and minimum marks “2” . Oil level is below the minimum mark Add oil up to the proper lever. |  |

| RECOMMENDED ENGINE OIL |  |
| --- | --- |
| Refer to the chart for selection of the oils suited to the atmospheric temperature. |  |
|  | API STANDARD: |  |
|  | API SE or higher grade |  |
| CAUTION: (Do not put in any chemical additives or use oils with a grade of CD or higher. (Be sure not to use oils labeled "ENERGY CONSERVING I" or higher. Engine oil also lubricates the clutch and additives could cause clutch slippage. (Be sure no foreign material enters the crankcase. |  |
| 4. Start the engine and let it warm up for a few minutes. |  |
| 5. Turn off the engine. |  |
| NOTE: Wait a few minutes until the oil settles before inspecting the oil level. |  |
| ENGINE OIL REPLACEMENT |  |
| 1. Start the engine and let it warm up for several minutes . |  |
| 2. Turn off the engine and place an oil pan under the engine. |  |
| 3. Remove : (Oil filer plug (Drain plug ( (Compression spring ( (Oil strainer ( (O-ring (Drain the crankcase of its oil. |  |
| 4. Install: (O-ring ( NEW (Compression spring ( (Oil strainer ( (Drain plug ( (Oil filer plug |  |
| NOTE : Check the drain plug O-ring. If damaged, replace it with a new one. |  |

| 5. Fill: (Crankcase |  |
| --- | --- |
|  | Oil quantity: |  |
|  | 1.4L |  |
| 6. Check: (Engine oil level Refer to "ENGINE OIL LEVEL INSPECTION" section |  |
| ENGINE OIL PRESSURE INSPECTION |  |
| Inspection steps: (Slightly loosen the oil check bolt ( (Start the engine and keep it idling until the oil begins to seep from the oil check bolt. If no oil comes out after one minute, turn the engine off so it will not seize. (Check oil passages and oil pump for dam age or leakage. (Start the engine after solving the problem (s), and recheck the oil pressure. (Tighten the oil check bolt to specification. |  |
| CAUTION: (Start the engine and check the oil pressure with the oil check bolt loosened. (Do not apply at high speeds more than specified when checking the pressure. |  |
| NOTE: Wipe any spilled oil off the engine. |  |
| 3.2.6COOLANT LEVEL INSPECTION |  |
| Inspect: |  |
| (Coolant level Coolant level should be between the maximum and minimum marks. Coolant level is below the "LOWER " level line Add soft water (tap water) up to the proper level. |  |
| CAUTION: Hard water or salt water is harmful to engine parts. Use only distilled water if soft water is not available. If you use tap water, make sure it is soft water. |  |
| 1. Start the engine and let it warm up for several minutes. |  |
| 2. Turn off the engine and inspect the coolant level again. |  |
| NOTE: Wait a few minutes until the coolant settles before inspecting the coolant level. |  |
| COOLANTRE PLACE MENT |  |
| Remove: (Front cover of ATV plastic body work. (Seat. |  |
| Remove: (Hose ( (reservoir tank) Drain the reservoir tank of its coolant. |  |
| Remove: (Drain bolt ( (Radiator cap |  |
| WARNING: Do not remove the radiator cap when the engine and radiator are hot. Scalding hot fluid and steam may be blown out under pressure, which could cause serious injury. When the engine has cooled, open the radiator cap as follows: Place a thick rag or a towel over the radiator cap. Slowly rotate the cap counterclockwise toward the detent. This allows any residual pressure to escape. When the hissing sound has stopped, press down on the cap while turning counterclockwise and remove it. |  |
| NOTE: (Remove the radiator cap after removing the drain bolt. |  |

| Clean: (Radiator Fill soft water into the filer neck support ( (reservoir tank). |  |
| --- | --- |
| 5. Install: (Gasket ( NEW (Drain bolt( |  |
| 6. Loosen: (Hose( |  |
| 7. Connect: (Hose (reservoir tank) |  |
| 8. Fill: (Radiator ( to specified level( ) Fill the coolant slowly, until the coolant comes out from the head hose. (Reservoir tank ( to maximum level ) |  |
|  | Recommended coolant: |  |
|  | High quality ethylene glycol anti-freeze containing corrosion inhibitors for aluminum engine. |  |
|  | Coolant ( and water ③ (soft water) : |  |
|  | Mixed ratio: min50% /max50% follow the instruction of the coolant |  |
|  | Total amount: |  |
|  | 2 L |  |
|  | Reservoir tank capacity: |  |
|  | 0.35L |  |
| Handling notes for coolant: Coolant is potentially harmful and should be handled with special care. |  |
| WARNING: splashes in your eyes: Thoroughly wash your eyes with water and consult a doctor. If coolant splashes on your clothes: (Quickly wash it away with water and then with soap and water. If coolant is swallowed: Vomit immediately and see a physician. |  |

| CAUTION: (Hard water or salt water is harmful to engine parts. Use only distilled water if soft water is not available. (If you use tap water, make sure it is soft water. (Do not use water containing impurities or oil. (Take care that no coolant splashes onto painted surfaces. If it does, wash them immediately with water. (Do not mix different types of ethylene glycol antifreeze containing corrosion inhibitors for aluminum engines. |  |
| --- | --- |
| 9. Tighten: (Hose Fill the coolant slowly to the specified level. |  |
| 10. Install: (Radiator cap |  |
| 11. Start the engine and let it warm up for several minutes. |  |
| 12. Stop the engine and inspect the level. |  |
| NOTE: Wait a few minutes until the coolant settles before inspecting the coolant level. |  |
| 13. Install: Remain parts. |  |

3.3CYLINDER HEAD

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 | Cylinder head removal Drain the coolant. Side panel Footrest board Carburetor Thermo unit lead Plug cap Crankcase breather hose Outlet hose (cylinder head) Breather hose (crankcase) Carburetor joint Joint O-ring | 1 1 2 1 1 1 1 2 | Remove the parts in order. Refer to "CARBURETOR" section . |

| 9 10 11 12 13 14 15 16 17 18 19 20 | Crankcase cover Plug/O-ring Cam sprocket cover/O-ring Valve cover (intake side)/O-ring Valve cover (exhaust side)/O-ring Timing chain tensioner assembly Timing chain tensioner gasket Breather plate Cam sprocket/Timing chain Cylinder head Cylinder head gasket Dowel pin | 1 1/1 1/1 1/1 1/1 1 1 1 1/1 1 1 2 | Refer to "CYLINDER HEAD REMOVAL AND INSTALLATION" section. Reverse the removal procedure for installation. |
| --- | --- | --- | --- |

| CYLINDER HEAD REMOVAL |  |
| --- | --- |
| 1. Align: "I" mark on the rotor (with stationary pointer on the crankcase cover ) NOTE: If any special mark found, contact the ATV manufacture via the agent for the parts and special instruction. |  |
| NOTE: Turn the primary sheave counterclockwise with a wrench and align the "I" mark with the cylinder head match mark when the piston is at TDC on the compression |  |
| 2. Loosen: (Bolt ( |  |
| 3. Remove: (Timing chain tensioner assembly (Timing chain tensioner gasket |  |
| 4. Remove: (Breather plate ( (Cam sprocket ③ (Timing chain④ |  |
| NOTE: (Fasten a safety w ire to the timing chain to prevent it from falling into the crankcase. (Remove the bolt ( while holding the rotor mounting bolt with a wrench. |  |
| 5. Remove: ( Cylinder head |  |
| NOTE: (Loosen the nuts in their proper loosening sequence. (Start by loosening each nut 1/2 turn until all are loose. |  |
| CYLINDER HEAD INSPECTION: |  |
| 1. Eliminate: (Carbon deposits (from combustion chambers) Use a rounded scraper. |  |
| NOTE: Do not use a sharp instrument to avoid damaging or scratching: (Spark plug threads (Valve seats |  |
| 2. Inspect: (Cylinder head Scratches/damage → Replace. |  |

| 3. Measure: (Cylinder head warpage Out of secification → Resurface . |  |
| --- | --- |
|  | Cylinder head warpage : |  |
|  | Less than 0.03 mm |  |
| Warpage measurement and resurfacement steps: (Place a straight edge and a feeler gauge across the cylinder head. (Measure the warpage. If the warpage is out of specification, resurface the cylinder head. ( Place a 400 ~ 600 grit wet abrasive pape on the surface plate, and resurface the head using a figure eight sanding patten. |  |
| NOTE: Rotate the cylinder head several times for an even resurfacement. |  |
| CYINDER HEAD INSTALLATION |  |
| 1. Install: (Gasket (cylinder head) NEW (Dowel pins (Cylinder head |  |
| NOTE: (Apply engine oil onto the nut threads. (Tighten the nuts in a crisscross pattern. |  |
| 2. Tighten: (Nuts (cylinder head) (Bolts (cylinder) |  |
| 3. Install: (Cam sprocket ( (Timing chain ( |  |
| Installing steps : (Turn the primary sheave counterclockwise until the TDC mark matches the stationary pointer . (Align the "I" mark on the cam sprocket with the stationary pointer on the cylinder head. NOTE: If any special mark found, contact the ATV manufacture via the agent for the parts and special instruction. (Fit the timing chain onto the cam sprocket and install the cam sprocket on the camshaft. |  |

| NOTE: (When installing the cam sprocket, keep the timing chain as tense as possible on the exhaust side. (Align the match mark on the cam sprocket with the stationary pointer on the cylinder head. (Align the pin on the cam shaft with the slot in the cam sprocket. |  |
| --- | --- |
| CAUTION: Do not turn the crankshaft during installation of the cam shaft. Dam age or improper valve timing will result. |  |
| (While holding the camshaft, temporarily tighten the bolts . |  |
| (Remove the safety wire from the timing chain. |  |
| 4. Install: (Breather plate ( (Plane washer ( |  |
| 5. Install: (Timing chain tensioner |  |
| Installing steps: (Remove the tensioner cap bolt ( and springs (. (Release the timing chain tensioner one-w ay cam ( and push the tensioner rod ( all the way in. (Install the tensioner with a new gasket (onto the cylinder. (Install the springs ( and cap bolt (. (Tighten the bolt (with gasket) to the specified torque . Bolt (chain tensioner) Cap bolt (timing chain tensioner) |  |
| 6. Tighten: (Bolt (cam sprocket) |  |
| 7. Check: (Valve timing Out of alignment → Adjust. |  |
| 8. Check: (Valve clearance Out of specification → Adjust. Refer to the "VALVE CLEARANCE ADJUSTMENT"section. |  |

3.4CAMSHAFT AND ROCKER ARMS

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
| 1 | Cam shaft and rocker arms removal Cylinder head Lock washer | 1 | Remove the parts in order. Refer to "CYLINDER HEAD" section. |
| 2 | Plate | 1 | Refer to "ROCKER ARM AND ROCKER |
| 3 | Rocker arm shaft (intake) | 1 | SHAFT REMOVAL AND INSTALLATION" section.. |
| 4 | Rocker arm shaft (exhaust) | 1 |  |
| 5 | Rocker arm | 2 |  |
| 6 | Camshaft | 1 | Refer to "CAMSHAFT INSTALLATION" |
| 7 | Locknut | 2 | section . |
| 8 | Adjuster | 2 |  |
| 9 | O-ring | 1 |  |
|  |  |  | Reverse the removal procedure for installation |

| ROCKER ARM AND ROCKER ARM SHAFTRE MOVAL |  |
| --- | --- |
| 1. Remove: (Rocker arm shaft (intake) (Rocker arm shaft (exhaust) |  |
| NOTE: Attach a rocker arm shaft puller bolt ( and weight ( to the rocker arm shaft and slide out the shaft. |  |
| CAM SHAFT INSPECTION |  |
| 1. Inspect: (Cam lobes Pitting/Scratches/Blue discoloration →Replace . |  |
| 2. Measure: (Cam lobes length and Out of specification → Replace. |  |
|  | Cam lobes length: |  |
|  | Intake: |  |
|  | 36 .545- 36 .645 mm |  |
|  | <Lim it: 36.45 mm> |  |
|  | 30.021-30.121 mm |  |
|  | <Lim it: 29.92 mm> |  |
|  | Exhaust: |  |
|  | 36 .547- 36 .647 mm |  |
|  | <Lim it: 36.45 mm> |  |
|  | 30.067- 30.167 mm |  |
|  | <Lim it: 29.97 mm> |  |
| 3. Inspect: (Cam shaft oil passage Stuffed → Blow out oil passage with compressed air. |  |
| ROCKER ARMS AND ROCKER ARM SHAFTS INSPECTION |  |
| 1. Inspect: (Cam lobe contact surface ( (Adjuster surface ( Wear/Pitting/Scratches/Blue discoloration→Replace. |  |

| Inspection steps: (Inspect the two contact areas on the rocker arms for signs of unusual wear. (Rocker arm shaft hole. (Cam-lobe contact surface. Excessive wear → Replace. (Inspect the surface condition of the rocker arm shafts. Pitting/scratches/blue discoloration → Replace or check lubrication. (Measure the inside diameter A of the rocker arm holes. Out of specification → Replace. |  |
| --- | --- |
|  | Inside diameter (rocker arm ): |  |
|  | 12.000- 12.018mm |  |
|  | < Lim it: 12.030 mm > |  |
| ( Measure the outside diameter B of the rocker arm shafts. Out of specification → Replace. |  |
|  | Outside diameter(rocker arm shaft): |  |
|  | 11.981-11.991 mm |  |
|  | <Limit: 11.95 mm> |  |
| CAMSHAFT AND ROCKER ARM |  |
| INSTALLATION |  |
| 1. Lubricate: (Cam shaft ( |  |
|  | Camshaft: |  |
|  | Molybdenum disulfide oil |  |
|  | Camshaft bearing: |  |
|  | Engine oil |  |
| 2. Install: (Plate( (Lockwasher ( NEW (Bolt ( |  |
| NOTE: Bend the lockwasher tabs along the bolt ( falts. |  |
| 3. Apply: (Molybdenum disulfide oil onto the rocker arm and rocker arm shaft. |  |
|  | Molybdenum disulfide oil |  |

| 4. Install: (Rocker arm ( (Rocker arm shaft ( (exhaust) |  |
| --- | --- |
| NOTE: Exhaust: Install the rocker arm shaft (exhaust) completely pushed in. |  |
| 5. Install: (Rocker arm ( (Rocker arm shaft ( (intake) |  |
| NOTE: Intake: Insert the guide shaft (8 mm) ( into the stud bolt hole in the cylinder head to the rocker arm shaft (intake). |  |
| CAUTION: Do not confuse the installation direction of rocker arm shaft. Be sure to install the threaded part facing outward. |  |

3.5VALVES AND VALVE SPRINGS

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 | Valves and valve springs removal Cylinder head Rocker arm , rocker arm shaft Valve cotters Spring retainer Valve spring (inner) Valve spring (Outer) Valve (intake) Valve (exhaust) Valve guide Spring seat | 4 2 2 2 1 1 2 2 | Remove the parts in order. Refer to "CYLINDER HEAD " section . Refer to "ROCKER ARM SHAFT AND ROCKER ARMS" section. Refer to "VALVES AND VALVE SPRINGS REMOVAL/INSTALLATION" section. Refer to "VALVES AND VALVE SPRINGS INSTALLATION" section Reverse the removal procedure for installation |

| VALVES AND VALVE SPRINGS REMOVAL |  |
| --- | --- |
| 1. Remove: ( Valve cotters ( |  |
| NOTE: Attach a valve spring compressor and attachment ( between the valve spring retainer and cylinder head to remove the valve cotters. |  |
| CAUTION: Do not compress so much as to avoid damage to the valve spring. |  |
| VALVE AND VALVE SPRINGS INSPECTION |  |
| 1. Measure: (Valve stem diameter Out of specification → Replace. |  |
|  | Valve stem diameter: |  |
|  | Intake: |  |
|  | 5.975-5.990mm |  |
|  | <Limit: 5.94mm> |  |
|  | Exhaust: |  |
|  | 5.960-5.975mm |  |
|  | <Limit: 5.92mm> |  |
| 2. Measure: (Runout (valve stem ) Out of specification → Replace. |  |
|  | (Runout limit: |  |
|  | 0.01 mm |  |
| 3. Measure: (Free length (valve spring) Out of specification → Replace. |  |
|  | Valve spring free length: |  |
|  | Inner spring: |  |
|  | 38.1 mm |  |
|  | <Limit: 36.1mm> |  |
|  | Outer spring: |  |
|  | 36.93 mm |  |
|  | <Limit: 35.0mm> |  |

| 4. Measure: (Spring tilt Out of specification → Replace. |  |
| --- | --- |
|  | Spring tilt limit: |  |
|  | 1.7mm (2.5º) |  |
| 5. Inspect: |  |
| ( Spring contact face |  |
| Wear/Pitting/Scratches → Replace. |  |
| 6. Measure: |  |
| (Valve guide inside diameter |  |
| Out of specification → Replace. |  |
|  | Valve guide inside diameter: |  |
|  | Intake: |  |
|  | 6.000-6.012 mm |  |
|  | <Limit: 6.05mm> |  |
|  | Exhaust: |  |
|  | 6.000-6.012 mm |  |
|  | <Limit: 6.05 mm> |  |
| 7. Measure: |  |
| Stem-to guide clearance= |  |
| Valve guide inside diameter- |  |
| Valve stem diameter |  |
| Out of specification → Replace the valve guide. |  |
|  | Stem-to-guide clearance limit: |  |
|  | Intake: |  |
|  | 0.08 mm |  |
|  | Exhaust: |  |
|  | 0.10 mm |  |
| VALVE SEATS INSPECTION |  |
| 1. Eliminate: |  |
| (Carbon deposits |  |
| (from the valve face and valve seat) |  |
| 2. Inspect: |  |
| (Valve seats |  |
| Pitting/wear → Reface the valve seat. |  |

| 3. Measure: |  |
| --- | --- |
| (Valve seat width |  |
| Out of specification → Reface the valve seat. |  |
|  | Valve seat width: |  |
|  | Intake: |  |
|  | 0.9-1.1mm |  |
|  | <Limit:1.6mm> |  |
|  | Exhaust: |  |
|  | 0.9-1.1mm |  |
|  | <Limit:1.6mm> |  |
| Measurement step: |  |
| (Apply Mechanic’s blueing dye (Dykem)( to the valve face. |  |
| (Install the valve into the cylinder head. |  |
| Press the valve through the valve guide and onto the valve seat to make a clear pattern. |  |
| (Measure the valve seat width. Where the valve seat and valve face made contact, blueing will have been removed. |  |
| (If the valve seat is too wide, too narrow, or the seat is not centered, the valve seat must be replaced. |  |
| 4. Lap: |  |
| (Valve face |  |
| (Valve seat |  |
| NOTE: |  |
| After replacing the valve seat, valve and valve guide, the valve seat and valve face should be lapped. |  |
| Lapping steps: |  |
| (Apply a coarse lapping com pound to the valve face. |  |
| CAUTION: |  |
| Do not let compound enter the gap between the valve stem and the guide. |  |
| (Apply molybdenum disulfide oil to the valve stem. |  |
| (Install the valve into the cylinder head. |  |
| (Turn the valve until the valve face and valve seat are evenly polished, then clean off al com pound. |  |
| NOTE: |  |
| For best lapping results, lightly tap the valve seat while rotating the valve back and forth between your hand. |  |

| (Apply a fine lapping compound to the valve face and repeat the above steps. |  |
| --- | --- |
| NOTE: |  |
| Make sure to clean off all compound from the valve face and valve seat after every lapping operation. |  |
| (Apply Mechanic’s blueing dye (Dykem) to the valve face. |  |
| (Install the valve into the cylinder head. |  |
| (Press the valve through the valve guide and onto the valve seat to make a clear pattern. |  |
| (Measure the valve seat with again. |  |
| VALVES AND VALVE SPRINGS |  |
| INSTALLATION |  |
| 1. Deburr: |  |
| (Valve stem end |  |
| Use an oilstone to smooth the stem end. |  |
| 2. Apply: |  |
| (Molybdenum disulfide oil |  |
| (onto the valve stem( and oil seal ( ) |  |
|  | Molybdenum disulfide oil |  |
| 3. Install: |  |
| (Valve spring seat ( |  |
| (Valve stem seal(NEW |  |
| (Valve ( |  |
| (into the cylinder head) |  |
| (Valve spring (under) ( |  |
| (Valve spring (outer) ( |  |
| (Spring retainer ( |  |
| NOTE: |  |
| Install the valve spring with the larger pitch facing upwards. |  |
| Smaller pitch |  |

| 4. Instal: |  |
| --- | --- |
| (Valve cotters ( |  |
| NOTE: |  |
| Install the valve cotters while com pressing the valve spring with a valve spring compressor and attachment (. |  |
| 5. Secure the valve cotters onto the valve stem by tapping lightly with a piece of wood. |  |
| CAUTION: |  |
| Do not hit so much as to damage the valve. |  |

3.6CYLINDER AND PISTON

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
|  | Cylinder and piston removal |  | Remove the parts in order. |
|  | Cylinder head |  | Refer to " CYLINDER HEAD " |
| 1 | Joint | 1 | section . |
| 2 | O-ring | 2 |  |
| 3 | Timing chain guide (exhaust side) | 1 | Refer to " PISTON RINGS, |
| 4 | Cylinder | 1 | PISTON AND CYLINDER INSTALLATION" section. |
| 5 | Dowel pin | 2 |  |
| 6 | Cylinder gasket | 1 |  |
| 7 | Piston pin circlip | 2 | Refer to "PISTON AND |
| 8 | Piston pin | 1 | PISTON RINGS REMOVAL" |
| 9 | Piston | 1 | section . |
| 10 | Piston ring (top) | 1 | Refer to "PISTON RINGS, |
| 11 | Piston ring (2nd) | 1 | PISTON AND CYLINDER |
| 12 | Side rail/Spacer | 2/1 | INSTALLATION " section . Reverse the removal procedure for installation . |

| PISTON AND PISTON RINGS REMOVAL |  |
| --- | --- |
| 1. Remove: |  |
| (Piston pin circlip ( |  |
| (Piston pin ( |  |
| (Piston ( |  |
| NOTE: |  |
| Before removing the piston pin circlip, cover the crankcase opening with a clean tow el or rag to prevent the circlip from falling into the crankcase cavity. |  |
| 2. Remove: |  |
| (Top ring |  |
| (2nd ring |  |
| (Oil ring |  |
| NOTE: |  |
| When removing the piston ring, open the end gap of the ring by fingers, and push up the other side of the ring. |  |
| CYLINDER INSPECTION |  |
| 1. Measure: |  |
| (Cylinder bore |  |
| Out of specification → Rebore or replace. |  |
| NOTE: |  |
| (Measure the cylinder bore with a cylinder bore gauge. |  |
| (Measure the cylinder bore in parallel to and a right angle to the crankshaft. Then, find the average of the measurements. |  |
|  | Cylinder bore: |  |
|  | 260;70.000- 70.014mm， 300;72.500- 72.514mm |  |
|  | < Limit:260;70.025mm，300;72.525> |  |
|  | < Difference limit between A,B and C :0.03m m > |  |
| 2. Measure: |  |
| (Warpage |  |
| Out of specification → Replace. |  |
|  | Cylinder warpage limit: |  |
|  | 0.03mm |  |

| PISTON AND PISTON PIN INSPECTION |  |
| --- | --- |
| 1. Measure: |  |
| (Piston skirt diameter |  |
| Out of specification → Replace . |  |
| 5.0mm from the piston bottom edge. |  |
|  | Valve skirt diameter: |  |
|  | 260; 69.965-69.980 mm 300; 72.465-72.480 mm |  |
|  | Oversize (2) |  |
|  | 260; 69.5 mm，300; 72.0 mm |  |
|  | Oversize (4) |  |
|  | 260;70.0 mm，260;72.5 mm |  |
| 2. Calculate: |  |
| (Piston-to-cylinder clearance |  |
| Piston-to-cylinder clearance= |  |
| Cylinder bore-Piston skirt diameter |  |
| Refer to “CYLINDER” section for cylinder bore measurement. |  |
| Out of specification → Replace the piston and piston rings as a set. |  |
|  | Piston-to-cylinder clearance: |  |
|  | 0.02-0.04mm |  |
| 3. Measure: |  |
| (Piston pin bore diameter |  |
| Out of specification → Replace. |  |
|  | Piston pin bore diameter: |  |
|  | 17.004-17.015mm |  |
|  | <Limit:17.045mm> |  |
| 4. Measure: |  |
| (Piston pin outside diameter |  |
| Out of specification → Replace. |  |
|  | Piston pin bore diameter: |  |
|  | 16.991-17.000mm |  |
|  | <Limit:16.975mm> |  |
| 5. Inspect: |  |
| (Piston pin |  |
| Blue discoloration/groove → Clean or replace. |  |

| PISTON RINGS INSPECTION |  |
| --- | --- |
| 1. Measure: |  |
| (Side clearance |  |
| Out of specification → Replace the piston and the piston rings as a set. |  |
| NOTE: |  |
| Eliminate the carbon deposits from the piston ring grooves and rings before measuring the side clearance. |  |
|  | Side clearance (piston ring): |  |
|  | Top ring: |  |
|  | 0.04- 0.08m m |  |
|  | <Limit: 0.12mm> |  |
|  | 2nd ring: |  |
|  | 0.03 - 0.07mm |  |
|  | <Limit: 0.12mm> |  |
| 2.Position: |  |
| (Piston ring into the cylinder |  |
| NOTE : |  |
| Push the ring with the piston crown so that the ring will be at a right angle to the cylinder bore. |  |
| 5.0mm |  |
| 3. Measure: |  |
| (End gap |  |
| (Out of specification → Replace. |  |
| NOTE: |  |
| You cannot measure the end gap on the expander spacer of the oil ring. If the oil ring rails show excessive gap, replace all three rings. |  |
|  | End gap: |  |
|  | Top ring: |  |
|  | 0.15-0.30mm |  |
|  | <Limit:0.45mm> |  |
|  | 2nd ring: |  |
|  | 0.30-0.45mm |  |
|  | <Limit:0.70m m> |  |
|  | Oil ring: |  |
|  | 0.20-0.70mm |  |
| PISTON RINGS, PISTON AND |  |
| CYLINDER INSTALLATION |  |
| 1. Install: |  |
| (Top ring ( |  |
| (2nd ring ( |  |
| (Side rails (oil ring) ( |  |
| (Expander spacer (oil ring) ( |  |

| NOTE: |  |
| --- | --- |
| (Make sure to install the piston rings so that the manufacturer’s m arks or numbers are located on the upper side of the rings. |  |
| (Lubricate the pistons and piston rings liberally with engine oil. |  |
| 2.Install: |  |
| (Piston ( |  |
| (Piston pin ( |  |
| (Piston pin clip ( NEW |  |
| NOTE: |  |
| (Apply engine oil to the piston pins. |  |
| (The " → " mark on the piston must face the exhaust side of the cylinder. |  |
| (Before installing the piston pin clip, cover the crankcase opening with a clean rag to prevent the piston pin clip from falling into the crankcase. |  |
| (Make sure to install each piston in its respective cylinder. |  |
| 3. Install: |  |
| (Gasket (cylinder) NEW |  |
| (Dowel pins |  |
| 4. Position: |  |
| (Piston rings |  |
| NOTE: |  |
| Offset the piston ring end gaps as shown. |  |
| Top ring end |  |
| Oil ring end (lower) |  |
| Oil ring end (upper) |  |
| 2nd ring end |  |

| 5. Lubricate: |  |
| --- | --- |
| (Piston outer surface |  |
| (Piston ring |  |
| (Cylinder inner surface |  |
|  | Engine oil |  |
| 6. Install: |  |
| (Cylinder |  |
| NOTE: |  |
| (Install the cylinder with one hand while com pressing the piston rings with the other hand. |  |
| (Pass the timing chain and timing chain guide (exhaust side) through the timing chain cavity. |  |

3.7V-BELT,CLUTCH AND SECONDARY/PRIMARY SHEAVE

CRANKCASE COVER (LEFT)

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
|  | Crankcase cover (left) removal |  | Remove the parts in order. |
| 1 | Crankcase cover (left) | 1 |  |
| 2 |  | 1 |  |
| 3 | Hose clamp B | 1 |  |
| 4 | Joint B | 1 |  |
| 5 | Air strainer B | 1 |  |
| 6 | Hose clamp A | 1 |  |
| 7 | Joint A | 1 |  |
| 8 | Air strainer A | 1 | Reverse the removal procedure for installation . |

PRIMARY SHEAVE

*Apply molybdenum disulfide grease

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
|  | V-belt, clutch and secondary/ |  | Remove the parts in order |
| 1 | primary sheave removal Nut/Plain washer | 1/1 | Refer to "PRIMARY SHEA VE |
| 2 | Primary fixed sheave | 1 | REMOVAL" section. |
| 3 | Nut | 1 | Refer to "SECONDARY SHEAVE |
| 4 | Clutch housing | 1 | AND V-BELT REMOVAL" |
| 5 | Clutch assembly | 1 | section. |
| 6 | V-belt | 1 | Refer to "SECONDARY SHEAVE |
| 7 | Primary sliding sheave | 1 | INSTALLATION" section. |
| 8 | Collar | 1 |  |
| 9 | Primary sheave cap | 1 | Refer to "PRIMARY SHEAVE |
| 10 | Cam | 1 | ASSEMBLY" section. |
| 11 | Weight | 8 |  |
| 12 | Slider | 4 | Refer to "PRIMARY SHEAVE |
| 13 | Spacer | 4 | ASSEMBLY" section. |
| 14 | Oil seal | 1 | Reverse the removal Procedure for installation. |

SECONDARY SHEAVE

**Apply lightweight lithium-soap base grease

| Order | Job name / Part name | Q ’ty | Remarks |
| --- | --- | --- | --- |
|  | Secondary sheave disassembly |  | Disassemble the parts in order. |
| 1 | Nut | 1 |  |
| 2 | Clutch carrier | 1 | Refer to "SECONDARY SHEAVE |
| 3 | Clutch shoe spring | 3 | DISASSEMBLY" section. |
| 4 | Compression spring | 1 |  |
| 5 | Spring seat | 1 | Refer to "SECONDARY SHEAVE |
| 6 | Guide pin | 4 | INSTALLATION " section . |
| 7 | Secondary sliding sheave | 1 |  |
| 8 | O-ring | 2 | Refer to "SECONDARY SHEAVE |
| 9 | Oil seal | 2 | INSTALLATION" section. |
| 10 | Secondary fixed sheave | 1 |  |
|  |  |  | Reverse the disassembly procedure for assembly. |

| PRIMARY SHEAVE REMOVAL |  |
| --- | --- |
| 1. Remove: |  |
| (Nut ((primary sheave) |  |
| (Plate washer |  |
| (Primary fixed sheave( |  |
| NOTE: |  |
| Loosen the nut (primary fixed sheave) while holding the primary fixed sheave with the rotor holder(. |  |
| SECONDARY SHEAVE AND V-BELT REMOVAL |  |
| 1. Remove: |  |
| (Nut ( (secondary sheave) |  |
| (Clutch housing ( |  |
| NOTE: |  |
| Loosen the nut (secondary sheave) while holding the clutch housing with the sheave holder(. |  |
| 2. Remove: |  |
| (Nut ( (clutch carrier) |  |
| CAUTION: |  |
| Do not remove the nut (clutch carrier) yet. |  |
| NOTE: |  |
| Loosen the nut (clutch carrier) one turn using the locknut wrench ( while holding the clutch carrier with the rotor holder(. |  |
| 3. Remove: |  |
| (Clutch assembly ( |  |
| (V-belt ( |  |
| NOTE: |  |
| Remove the V-belt from the primary sheave side with clutch assembly. |  |

| SECONDARY SHEAVE DISASSEMBLY |  |
| --- | --- |
| 1. Remove: |  |
| ( Nut ( (secondary sheave) |  |
| NOTE: |  |
| Loosen the nut ( while attaching the clutch spring compressor ( and clutch spring holder arm ( and release the compressed spring after removing the nut. |  |
| CAUTION: |  |
| Use the spacer ( (diameter:￠30mm thickness: 2-3mm). |  |
| CLUTCH INSPECTION |  |
| 1.Measure: |  |
| (Clutch shoe thickness |  |
| Scratches → Glaze using coarse sandpaper. |  |
| Wear /Damage → Replace |  |
|  | Clutch shoe thickness: |  |
|  | 3.0mm |  |
|  | <Limit:2.0mm> |  |
| NOTE: |  |
| (After using the sandpaper, clean off the polished particles. |  |
| (Inspect the other clutch shoes. |  |
| (Replace all three as a set. |  |
| V-BELT INSPECTION |  |
| 1.Inspect: |  |
| (V-belt ( |  |
| Cracks/Wear /Scaling /Chipping → Replace. |  |
| Oil/Grease → Check primary sheave and secondary sheave. |  |
| 2. Measure: |  |
| (V-belt width ( |  |
| Out of specification → Replace |  |
|  | V-belt width: |  |
|  | 22.6mm |  |
|  | (Limit:21.0mm) |  |

| WEIGHT INSPECTION |  |
| --- | --- |
| 1. Inspect: |  |
| ( Weight minimum outside diameter |  |
| Cracks/Wear /Scaling /Chipping → Replace. |  |
| Out of specification → Replace |  |
|  | Weight out side diameter: |  |
|  | 20.0 mm |  |
|  | <Limit: 19.5mm> |  |
| SECOMDARY SHEAVE INSPECTION |  |
| 1. Inspect: |  |
| (Secondary fixed sheave smooth operation |  |
| (Secondary sliding sheave smooth operation |  |
| 2. Inspect: |  |
| (Torque cam groove ( |  |
| Wear /Damage → Replace. |  |
| 3. Inspect: |  |
| (Guide pin ( |  |
| Wear /Damage → Replace. |  |
| PRIMARY SHEAVE ASSEMEBLY |  |
| 1. Clean: |  |
| (Primary sliding sheave face ( |  |
| (Primary fixed sheave face ( |  |
| (Collar ( |  |
| (Weight ( |  |
| (Primary sliding sheave cam face |  |
| NOTE: |  |
| Remove any excess grease. |  |
| 2. Install: |  |
| (Weight ( |  |
| (Collar ( |  |
| NOTE: |  |
| (Apply molybdenum disulfide grease to all of the outside of the weight and install. |  |
| (Apply lightweight lithium-soap base grease to the inside of the collar. |  |
| 3. Install: |  |
| (Spacer ( |  |
| (Slider ( |  |
| (Cam ( |  |
| (Primary sliding sheave cap. |  |
| SECOMDARY SHEAVE INSTALLATION |  |
| 1. Apply: |  |
| (Lightweight lithium-soap base grease |  |
| (to the secondary sliding sheave ( inner surface, grease nipple groove, and oil seals) |  |
| ( Lightweight lithium-soap base grease |  |
| (to the bearings, oil seals and inner surface of the secondary fixed sheave ( ) |  |
| 2. Install: |  |
| (Secondary sliding sheave ( |  |
| NOTE: |  |
| Install the secondary sliding sheave (using the oil seal guide ( to the secondary fixed sheave(. |  |
| 3. Install: |  |
| (Guide pin( |  |
| 4. Apply: |  |
| ( Lightweight lithium-soap base grease |  |
| (to the guide pin sliding groove (, and oil seal ( NEW） |  |
| 5. Install: |  |
| (Secondary sheave complete ( |  |
| (Compression spring |  |
| (Clutch carrier ( |  |
| NOTE: |  |
| Temporarily tighten the nut (while attaching the clutch spring holder ( and clutch spring holder arm ( and compress the spring. |  |

| CAUTION: |  |
| --- | --- |
| Use the spacer ( (30mm, thickness: 2-3mm). |  |
| 6. Install: |  |
| (V-belt ( |  |
| (Clutch assembly ( |  |
| NOTE: |  |
| Install the V-bet with clutch assembly to the primary sheave side. |  |
| CAUTION: |  |
| Never smear grease to the V-belt, secondary sheave and clutch. |  |
| 7. Install: |  |
| (Nut ( (clutch carrier) |  |
| NOTE: |  |
| Tighten the nut (clutch carrier), using the locknut wrench ( while holding the clutch carrier with the rotor holder ( |  |
| 8. Install: |  |
| (Clutch housing ( |  |
| (Nut (clutch housing) ( |  |
| NOTE: |  |
| Tighten the nut (clutch housing),using the sheave holder (). |  |
| 9. Set: |  |
| (V- belt ( |  |
| NOTE: |  |
| Move the V-belt to minimum diameter of the primary sheave (, maximum diameter of the secondary sheave ( and make the V-belt tense. |  |

3.8A.C. MAGNETO AND STARTER CLUTCH

MAGNETO COVER AND STATOR COIL

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
|  | Magneto cover and stator coil removal Drain the engine oil. |  | Remove the parts in order. Refer to "ENGINE OIL REPLACEMENT" section. NOTE: Disconnect the couplers. Reverse the removal procedure for installation. |
| 1 | Couplers (A.C. magneto lead) | 2 |  |
| 2 | Exhaust pipe | 1 |  |
| 3 | Exhaust pipe gasket | 1 |  |
| 4 | Magneto cover | 1 |  |
| 5 | Gasket (magneto cover) | 1 |  |
| 6 | Dowel pins | 2 |  |
| 7 | Stator coil | 1 |  |
| 8 | Pick up coil | 1 |  |

A. C. MAGNETO AND STARTER CLUTCH

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
| 1 2 3 4 5 6 | A.C. magneto and starter clutch removal Rotor Shaft (idle gear) Idler gear Starter one way clutch assembly Woodruff key Starter wheel gear | 1 1 1 1 1 1 | Remove the parts in order. Refer to "A.C. MAGNETO ROTOR REMOVAL /INSTALLATION" section. Refer to "ROTOR INSTALLATION" section. Reverse the removal procedure for installation. |

| A.C. MAGNETO ROTOR REMOVAL |  |
| --- | --- |
| 1. Remove: |  |
| (Nut ( (rotor) |  |
| (Plain washer( |  |
| NOTE: |  |
| (Loosen the nut (rotor) (while holding the rotor with a sheave holder( . |  |
| (Do not allow sheave the holder touch to the projection on the rotor. |  |
| 2. Remove: |  |
| (Rotor ( |  |
| (Woodruff key |  |
| NOTE: |  |
| (Remove the rotor (using the flywheel puller. |  |
| (Center the flywheel puller over the rotor. |  |
| Make sure after installing the holding bolts that the clearance between the flywheel puller and the rotor is the same everywhere. If necessary, one holding bolt may be turned out slightly to adjust the flywheel puller's position. |  |
| CAUTION: |  |
| Cover the crankshaft end with the box wrench for protection. |  |
| STARTER DRIVE GEAR INSPECTION |  |
| 1. Inspect: |  |
| (Starter idle gear teeth |  |
| (Starter drive gear teeth |  |
| (Starter wheel gear teeth |  |
| Burrs /chips /roughness /wear → Replace. |  |
| 2. Check: |  |
| (Starter clutch operation |  |
| Push the dowel pins to the arrow direction. |  |
| Unsmooth operation → Replace. |  |
| Checking steps: |  |
| (Hold the starter clutch. |  |
| (When turning the starter wheel gear clockwise, the starter clutch and the starter wheel gear should be engaged. |  |
| (If not, the starter clutch is faulty. Replace it. |  |
| (When turning the starter wheel gear counter clockwise, it should turn freely. |  |
| (If not, the starter clutch is faulty. Replace it. |  |

| A.C. MAGNETO ROTOR INSTALLATION |  |
| --- | --- |
| 1. Install: |  |
| (Starter wheel gear (. |  |
| (Woodruff key ( |  |
| NOTE: |  |
| Install the starter wheel gear(, then install the woodruff key(. |  |
| 2. Install: |  |
| ( Rotor ( |  |
| ( Plain washer |  |
| NOTE: |  |
| (Clean the tapered portion of the crankshaft and the rotor hub. |  |
| (When installing the magneto rotor, make sure the woodruff key is properly seated in the key way of the crankshaft. |  |
| 3.Tighten: |  |
| (Nut(rotor)( |  |
| NOTE: |  |
| Tighten the nut (rotor)( while holding the magneto rotor( with a sheave holder(. |  |

3.9OIL PUMP

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
|  | Oil pump removal |  | Remove the parts in order. |
|  | A.C. magneto |  | Refer to "A.C. MAGNETO AND STARTER |
| 1 | Cover | 1 | CLUTCH" section. |
| 2 | Pump driven gear | 1 |  |
| 3 | Dowel pin | 1 |  |
| 4 | Oil pump assembly | 1 |  |
| 5 | Gasket | 1 |  |
| 6 | Impeller shaft gear | 1 |  |
| 7 | Dowel Pin | 1 |  |
| 8 | Shaft | 1 |  |
|  |  |  | Reverse the removal procedure for installation. |

| OIL PUMP INSPECTION |  |
| --- | --- |
| 1. Inspect: |  |
| (Drive gear (oil pump) ( |  |
| (Pump housing |  |
| (Pump housing cover |  |
| Wear /cracks/ damage → Replace. |  |
| 2. Measure: |  |
| ( Tip clearance |  |
| (between the inner rotor ( and the outer rotor() |  |
| (Side clearance |  |
| (between the outer rotor ( and the pump housing ( ) |  |
| (Housing and rotor clearance |  |
| (between the pump housing ( and the rotors ( () |  |
| Out of specification → Replace the oil pump assembly. |  |
|  | Tip clearance : |  |
|  | 0.10-0.34 mm <Limit: 0.40mm> |  |
|  | Side clearance : |  |
|  | 0.013-0.036mm <Limit:0.15mm> |  |
|  | Housing and rotor clearance : |  |
|  | 0.04-0.09 mm <Limit: 0.15mm> |  |

3.10CRANKCASE AND CRANKSHAFT

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
| 1 2 | Crankcase and crankshaft removal Engine removal Cylinder head Cylinder, and piston V-belt, clutch, secondary/ primary sheave A.C. magneto and starter clutch Oil pump Water pump Rear wheel Bolt O- ring | 1 1 | Remove the parts in the order. Refer to "ENGINE REMOVAL" section. Refer to "CYLINDER HEAD" section. Refer to "CYLINDER AND PISTION" section. Refer to "V BELT, CLUTCH AND SECONDARY/ PRIMARY SHEAVE"section. Refer to "A.C. MAGNETO AND STARTER CLUTCH" section. Refer to "OIL PUMP" section. Refer to "WATER PUMP" section. Refer to "REAR WHEEL AND REAR BRAKE" section. |

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
| 3 4 5 6 7 8 9 10 | Timing chain guide (intake) Crankcase (right) Dowel pin Crankshaft assembly Timing chain Crankcase (left) Oil seal Oil seal | 1 1 2 1 1 1 1 | Refer to "CRANKSHAFT INSTALLATION" section. Refer to "CRANKSHAFT REMOVAL/ INSTALLATION" section. Reverse the removal procedure for installation. |

| CRANKSHAFT REMOVAL |  |
| --- | --- |
| 1. Remove: |  |
| (Crankshaft assembly |  |
| (Timing chain |  |
| NOTE: |  |
| (Before removing the crankshaft assembly, remove the timing chain from the crankshaft sprocket. |  |
| (If the timing chain hooks to the crankshaft sprocket, the crankshaft cannot be removed. |  |
| CRANKSHAFT INSPECTION |  |
| 1. Measure: |  |
| (Crankshaft runout |  |
| Out of specification → Replace crankshaft and/or bearing. |  |
| NOTE: |  |
| Measure the crankshaft runout with the crankshaft assembly running slowly. |  |
|  | Runout limit: |  |
|  | 0.03 mm |  |
| 2. Measure: |  |
| (Big end side clearance |  |
| Out of specification → Replace big end bearing, crank pin and/or connecting rod. |  |
|  | Big end side clearance: |  |
|  | 0.35-0.85 mm |  |
| 3. Measure: |  |
| (Crank width |  |
| Out of specification → Replace crankshaft. |  |
|  | Crank width: |  |
|  | 59.95-60.00 mm |  |

| 4. Inspect: |  |
| --- | --- |
| (Crankshaft sprocket ( |  |
| Wear/ Damage → Replace crankshaft. |  |
| (Bearing ( |  |
| Wear/ Crack /Damage → Replace crankshaft. |  |
| (Pump drive gear ( |  |
| Wear/ Damage → Replace crankshaft. |  |
| 5. Inspect: |  |
| (Crankshaft journal |  |
| Clogged → Blow out the journal with compressed air. |  |
| CRANKCASE INSTALLATION |  |
| 1. Clean all the gasket mating surface and crankcase mating surface thoroughly. |  |
| 2. Apply: |  |
| (Sealant |  |
| (onto the crankcase mating surfaces) |  |
| NOTE: |  |
| DO NOT ALLOW any sealant to come into contact with the oil gallery. |  |
| 3. Install: |  |
| (Dowel pins |  |
| (Timing chain ( |  |
| NOTE: |  |
| Install the timing chain not to be seen through the crankshaft hole on the crankcase (left)(. |  |

3.11COOLING SYSTEM

3.11.1RADIATOR

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
|  | Radiator removal Drain the coolant. |  | Remove the parts in order. Refer to "COOLANT REPLACEMENT" section. |
| 1 | Fan motor leads | 2 |  |
| 2 | Thermo switch leads | 2 |  |
| 3 | hose (radiator) | 1 |  |
| 4 | Outlet hose (radiator) | 1 |  |
| 5 | Inlet hose (radiator) | 1 |  |
| 6 | Radiator | 1 |  |
| 7 | Radiator cap | 1 |  |
| 8 | Radiator filler neck | 1 |  |
|  |  |  | Reverse the removal procedure for installation. |

| INSPECTION |  |
| --- | --- |
| 1. Inspect: |  |
| (Radiator ( |  |
| Obstruction → Blow out with compressed air through the rear of the radiator. |  |
| Flattened fins → Repair or replace. |  |
| If flattened over the 20% of radiator fin, repair or replace the radiator. |  |
| CAUTION: |  |
| Use only specified adhesive to repair the radiator. |  |
| 2. Inspect: |  |
| (Radiator hoses |  |
| (Radiator pipes |  |
| Cracks/damage → Replace. |  |
| 3. Measure: |  |
| (Radiator cap opening pressure |  |
| (Radiator cap opens at a pressure below the specified pressure → Replace. |  |
|  | Radiator cap opening pressure: |  |
|  | 110-140kPa |  |
|  | (1.1-1.4kg/cm2 , 1.1-1.4 bar) |  |
| Measurement steps: |  |
| (Attach the radiator cap tester (and adapter ( to the radiator cap (. |  |
| (Apply the specified pressure for 10 seconds, and make sure there is no pressure drop. |  |
| 4. Inspect: |  |
| (Fan motor assembly |  |
| Damage → Replace. |  |
| Malfunction → Check and repair. |  |
| Refer to "COOLING SYSTEM ". |  |
| 5. Inspect: |  |
| (Pipes |  |
| Cracks/damage → Replace. |  |

3.11.2WATER PUMP

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
|  | Water pump removal |  | Remove the parts in order. |
|  | Drain the coolant. |  | Refer to "COOLANT REPLACEMENT" section. |
|  | A.C. magneto |  | Refer to "A.C. MAGNETO AND STARTER CLUTCH" section. |
| 1 | lmpeller shaft gear | 1 |  |
| 2 | Dowel pin/plain washer | 1/1 |  |
| 3 | Shaft | 1 | Refer to "WATER PUMP INSTALLATION" |
| 4 | Outlet hose (radiator) | 1 | section. |
| 5 | Housing cover | 1 |  |
| 6 | Housing cover gasket | 1 |  |
| 7 | Water pump housing | 1 |  |
|  |  | 1 |  |

| Order | Job name/Part name | Q’ty | Remarks |
| --- | --- | --- | --- |
| 8 9 10 | Impeller shaft O-ring O-ring | 1 1 1 | Refer to “WATER PUMPINSTALLATION” section. Reverse the removal procedure for installation. |

| NOTE: |  |
| --- | --- |
| (It is not necessary to disassemble the water pump, unless there is an abnormality such as excessive change in coolant temperature and/ or level, discoloration of coolant, or milky transmission oil. |  |
| (If necessary, replace water pump as an assembly. |  |
| INSPECTION |  |
| 1. Inspect: |  |
| (Impeller shaft |  |
| Wear/damage → Replace. |  |
| Fur deposits → Clean. |  |
| 2. Inspect: |  |
| (Impeller shaft gear |  |
| Wear/damage → Replace. |  |
| 3. Inspect: |  |
| (Mechanical seal ( |  |
| Damage/worn/wear → Replace. |  |
| WATER PUMP INSTALLATION |  |
| 1. Install: |  |
| (Mechanical seal ( NEW |  |
| Installation steps: |  |
| (Apply the bond to the outside of the mechanical seal. |  |
| (Install the mechanical seal by using the mechanical seal installer ( and middle shaft bearing driver ( |  |
| 2. Install: |  |
| (Mechanical seal ( NEW |  |
| Apply coolant to the outside of the mechanical seal before installing. |  |
| NOTE: |  |
| Do not smear any oils or grease on the ring side of the mechanical seal. |  |

| 3. Inspect: |  |
| --- | --- |
| (Mechanical sea , slip ring side ( |  |
| Inspect the slip ring side of the mechanical seal and the impeller ( for level installation. |  |
| Incorrect level → Reinstall. |  |
| 4. Install: |  |
| (Impeller shaft( |  |
| (Circ lip ( NEW |  |
| Installation steps: |  |
| (Apply a small amount of grease to the impeller shaft tip. |  |
| (Install the impeller shaft while turning it. Use care so that the oil seal is not damaged or the spring does not slip off its position. |  |
| NOTE: |  |
| After installing the impeller shaft, check it for smooth rotation. |  |
| 5.Install: |  |
| (O-ring(NEW |  |
| 6. Install: |  |
| (Water pump housing |  |
| (Housing cover |  |
| 7. Install: |  |
| (Shaft( |  |
| Align the slot on the impeller shaft with the projection on the shaft when installing. |  |

3.11.3THERMOSTAT

| Order | Job name/ Part name | Q'ty | Remarks |
| --- | --- | --- | --- |
|  | Thermostat removal Drain the coolant |  | Remove the parts in order. Refer to "COOLANT REPLACEMENT" section. |
| 1 | Clip | 1 |  |
| 2 | Hose | 1 |  |
| 3 | Hose clamp | 1 |  |
| 4 | Inlet hose (radiator) | 1 |  |
| 5 | Thermostatic cover | 1 | Refer to "THERMOSTAT INSTALLATION" |
| 6 | Thermostatic valve | 1 | section. |
|  |  |  | Reverse the removal procedure for installation. |

| INSTALLATION |  |
| --- | --- |
| 1. Inspect: |  |
| (Thermostatic valve |  |
| Valve does not open at 70.5-73.5℃→Replace. |  |
| Inspection steps: |  |
| (Suspend the thermostatic valve in a vessel. |  |
| (Place a reliable thermometer in water. |  |
| ( Observe the thermometer, while continually stirring the water. |  |
| (Thermostatic valve |  |
| (Vessel |  |
| (Thermometer |  |
| (Water |  |
| A CLOSE |  |
| B OPEN |  |
| NOTE: |  |
| The thermostatic valve is sealed and its setting requires specialized work. If its accuracy is in doubt, replace. A faulty unit could cause serious over-heating or over cooling. |  |
| 2.Inspect: |  |
| (Thermostatic cover |  |
| Cracks /damage → Replace. |  |
| INSTALLATION |  |
| 1. Install: |  |
| (Thermostatic valve |  |
| (Thermostatic cover |  |

| 3.12CARBURETOR （ATV260/300） |
| --- |
| WARNING Gasoline is extremely flammable and explosive under certain conditions. Always stop the engine and refuel outdoors or in a well ventilated area. Do not smoke or allow open flames or sparks in or near the area where refueling is performed or where gasoline is stored. If you get gasoline in your eyes or if you swallow gasoline, see your doctor immediately. If you spill gasoline on your skin or clothing, immediately wash it off with soap and water and change clothing. Never start the engine or let it run in an enclosed area. Gasoline powered engine exhaust fumes are poisonous and can cause loss of consciousness and death in a short time. Never drain the float bowl when the engine is hot. Severe burns may result. CARBURETOR REMOVEL |
| 1. Remove: |  |
| (Auto choke lead coupler |  |
| 2. Remove: |  |
| (Fuel hose |  |
| 3. Remove: |  |
| (Nut① |  |
| (Throttle cable |  |
| 4.Lossen: |  |
| (Bolt② |  |
| (Bolt③ |  |
| 5. Remove: |  |
| (Carburetor assy |  |
| CARBURETOR DISASSEMBLY/ INSPECTION |  |
| 6.Auto choke inspection |  |
| (Ambient temperature lower than 45℃) |  |
| (Connect auto choke unit leads to the 12V battery for 5 minutes. |  |
| (Connect pipe to the starter①, and blow it with the mouth etc. |  |
| Possible→Replace auto choke unit. |  |
| Impossible→Good condition. |  |
| ( Remove auto choke unit leads to the 12V battery for 30 minutes. |  |
| (Connect pipe to the starter①, and blow it with the mouth etc. |  |
| Possible→Good condition. |  |
| Impossible→Replace auto choke unit. |  |
| 7. Remove: |  |
| (Blot① |  |
| (Auto choke unit② |  |
| 8. Auto choke unit inspection: |  |
| (Piston① |  |
| (Jet needle② |  |
| Wear→Replace. |  |
| 9.Install: |  |
| (Auto choke unit |  |
| VACUUM CHAMBER |  |
| 10.Remove: |  |
| (Cover① |  |
| 11.Remove: |  |
| (Diaphragm spring① |  |
| (Piston valve② |  |
| 12.Inspection: |  |
| (Jet needle |  |
| Wear→Replace. |  |
| (Piston valve |  |
| Wear→Replace. |  |
| Check the jet needle for stepped wear. |  |
| Check the vacuum piston for wear or damage. |  |
| Check the diaphragm for holes, deterioration or |  |
| damage. Check the vacuum piston for smooth operation up and down in the carburetor body. |  |
| FLOAT AND JETS |  |
| 13.Remove: |  |
| (Float chamber① |  |
| WARNING Never drain the float bowl when the engine and the exhaust system are hot. Severe burns may result. |  |
| (Float② |  |
| (Needle valve③ |  |
| 14.Inspection: |  |
| (Needle valve |  |
| Wear→Replace. |  |
| Check the float valve and valve seat for scoring |  |
| scratches, clogging or damage. |  |
| check the tip of the float valve, where it contacts the |  |
| valve seat, for stepped wear or contamination. |  |
| check the operation of the float valve. |  |
| 15.Remove: |  |
| (Pilot jet |  |
| Check the pilot jet for wear or damage. Clean the |  |
| pilot jet with cleaning solvent and blow this open |  |
| with compressed air. |  |
| 16.Remove: |  |
| (Main jet |  |
| Check the main jet for wear or damage. Clean the |  |
| main jet with cleaning solvent and blow this open |  |
| with compressed air. |  |
| 17.Remove: |  |
| (Main nozzle |  |
| Check the main nozzle for wear or damage. Clean |  |
| the main nozzle with cleaning solvent and blow this |  |
| open with compressed air. |  |
| 18.Remove: |  |
| (Pilot screw set |  |
| Turn the pilot screw in and carefully count the |  |
| number of turn until it seats lightly. Make a note |  |
| of this to use as a reference when reinstalling the pilot screw. |  |
| AIR CUT-OFF VALVE |  |
| 19.Remove: |  |
| (Cover① |  |
| (Compressing spring② |  |
| (Diaphragm③ |  |
| 20.Inspection: |  |
| (Compressing spring |  |
| Distortion→Replace. |  |
| (Diaphragm |  |
| Wear→Replace. |  |
| 21. Reverse the removal procedure for installation. |  |
| ACCERERATING PUMP |  |
| 22.Remove: |  |
| (Cover① |  |
| Check the vacuum piston for wear or damage. |  |
| 23.Inspection: |  |
| (Compressing spring① |  |
| Distortion→Replace. |  |
| (Diaphragm② |  |
| Wear→Replace. |  |
| 24. Reverse the removal procedure for installation. |  |

| 3.12CARBURETOR(ATV400-2/ATV400-2B) |  |
| --- | --- |
| 1. Remove: |  |
| (Fuel hose |  |
| 2. Remove: |  |
| (Manual enriching starter rope① |  |
| 3. Remove: |  |
| (Nut② |  |
| (Throttle cable |  |
| 4.Lossen: |  |
| (Bolt③ |  |
| (Bolt④ |  |
| 5. Remove: |  |
| (Carburetor assy |  |
| 6.Remove: |  |
| (Cover① |  |
| 7.Remove: |  |
| (Diaphragm spring① |  |
| (Piston valve② |  |
| 8.Inspect: |  |
| (Jet needle |  |
| Wear→Replace. |  |
| (Piston valve |  |
| Wear→Replace. |  |
| 9.Remove: |  |
| (Float chamber① |  |
| (Float② |  |
| (Needle valve③ |  |
| 10.Inspect: |  |
| (Needle valve |  |
| Wear→Replace. |  |
| 11.Remove: |  |
| (Idling jet |  |
| 12.Remove: |  |
| (Pilot jet |  |
| 13.Remove: |  |
| (Main jet |  |
| 14.Remove: |  |
| (Main nozzle |  |
| 15.Remove |  |
| (Mixture adjusting screw |  |
| 16. Remove |  |
| (Nut① |  |
| (Throttle valve mounting arm② |  |
| (Torsion-bar spring③ |  |
| (Gasket④ |  |
| 17.Remove： |  |
| (Screws①&② |  |
| (Throttle valve mounting bracket③ |  |
| 18. Reverse the removal procedure for installation. |  |

NOTES